An Aldus/Microsoft Technical Memorandum:  8/8/88    Page 1          An Aldus/Microsoft Technical Memorandum:  8/8/88    Page 1
          
          
          
          Preface
          
          
          This memorandum  has been prepared jointly by Aldus and Microsoft
          in conjunction  with leading scanner vendors and other interested
          parties.   This document  does not  represent a commitment on the
          part of  either Microsoft  or Aldus  to provide  support for this
          file format  in any  application.   When responding  to  specific
          issues raised  in this memo, or when requesting additional tag or
          field assignments, please address your correspondence to either:
          
               Developers_ Desk    Windows Marketing Group
               Aldus Corporation   Microsoft Corporation
               411 First Ave. South     16011 NE 36th Way
               Suite 200 Box 97017
               Seattle, WA  98104  Redmond, WA  98073-9717
               (206) 622-5500 (206) 882-8080
          
          
          
          Revision Notes
          
          This revision  replaces _TIFF  Revision 4._   Sections in italics
          are new or substantially changed in this revision.  Also new, but
          not in italics, are Appendices F, G, and H.
          
          The major enhancements in TIFF 5.0 are:
          
          1.   Compression of  grayscale and  color images, for better disk
          space utilization.  See Appendix F.
          
          2.   TIFF Classes_restricted  TIFF subsets  that can simplify the
          job of  the TIFF  implementor.   You may  wish to scan Appendix G
          before reading the rest of this document.   In fact, you may want
          to use  Appendix G as your main guide, and refer back to the main
          body of  the specification  as needed for details concerning TIFF
          structures and field definitions.
          
          3.   Support for  _palette color_   images.  See the TIFF Class P
          description  in   Appendix  G,   and  the   new  ColorMap   field
          description.
          
          4.   Two new  tags that  can be  used to  more fully  define  the
          characteristics of  full color  RGB data, and thereby potentially
          improve the quality of color image reproduction.  See Appendix H.
          
          The organization  of the  document has also changed slightly.  In
          particular, the  tags are  listed in  alphabetical order,  within
          several categories, in the main body of the specification.
          









          TIFF 5.0                                          page 2          TIFF 5.0                                          page 2


          As always,  every attempt  has been  made to add functionality in
          such a  way as  to minimize  incompatibility problems  with older
          TIFF software.   In  particular, many  TIFF  5.0  files  will  be
          readable even  by older  applications that  assume TIFF 4.0 or an
          earlier version  of the  specification.   One exception  is  with
          files that  use the  new TIFF  5.0 LZW  compression scheme.   Old
          applications will  have to  give up  in this case, of course, and
          will do so _gracefully_ if they have been following the rules.
          
          We  are  grateful  to  all  of  the  draft  reviewers  for  their
          suggestions.   Especially helpful  were Herb  Weiner  of  Kitchen
          Wisdom  Publishing   Company,  Brad  Pillow  of  TrueVision,  and
          engineers from Hewlett Packard and Quark.  Chris Sears of Magenta
          Graphics provided information which is included as Appendix H.
          
          
          Abstract
          
          This document  describes TIFF,  a tag  based file  format that is
          designed to promote the interchange of digital image data.
          
          The fields  were defined  primarily with  desktop publishing  and
          related applications  in mind, although it is possible that other
          sorts of imaging applications may find TIFF to be useful.
          
          The general  scenario for  which TIFF  was invented  assumes that
          applications software  for scanning  or painting  creates a  TIFF
          file, which  can then  be read and incorporated into a _document_
          or _publication_   by an application such as a desktop publishing
          package.
          
          TIFF is  not a printer language or page description language, nor
          is it intended to be a general document interchange standard. The
          primary design  goal was  to provide  a rich  environment  within
          which the exchange of image data between application programs can
          be accomplished.   This  richness is  required in  order to  take
          advantage of  the varying  capabilities of  scanners and  similar
          devices.  TIFF is therefore designed to be a superset of existing
          image file  formats for  _desktop_   scanners (and paint programs
          and anything  else that  produces images with pixels in them) and
          will be enhanced on a continuing basis as new capabilities arise.
          A high  priority has been given to structuring the data in such a
          way as  to minimize  the pain  of future  additions.    TIFF  was
          designed to be an extensible interchange format.
          
          Although TIFF  is claimed  to be  in some sense a rich format, it
          can easily  be used for simple scanners and applications as well,
          since the  application developer  need only be concerned with the
          capabilities that he requires.
          
          TIFF is intended to be independent of specific operating systems,
          filing systems,  compilers, and processors.  The only significant
          assumption is  that the  storage medium supports something like a
          _file,_   defined as  a sequence  of 8-bit bytes, where the bytes









          TIFF 5.0                                          page 3          TIFF 5.0                                          page 3


          are numbered  from 0  to N.   The  largest possible  TIFF file is
          2**32 bytes  in length.   Since TIFF uses pointers (byte offsets)
          quite liberally,  a TIFF  file is  most easily read from a random
          access device  such as a hard disk or flexible diskette, although
          it should  be possible  to read  and write TIFF files on magnetic
          tape.
          
          The recommended  MS-DOS, UNIX,  and OS/2  file extension for TIFF
          files is  _.TIF._   The recommended Macintosh filetype is _TIFF_.
          Suggestions for  conventions in  other computing environments are
          welcome.
          
          
          1) Structure
          
          In TIFF, individual fields are identified with a unique tag. This
          allows particular fields to be present or absent from the file as
          required by the application.  For an explanation of the rationale
          behind using a tag structure format, see Appendix A.
          
          A TIFF file begins with an 8-byte _image file header_ that points
          to one  or  more  _image  file  directories._    The  image  file
          directories contain  information about  the images,  as  well  as
          pointers to the actual image data.
          
          See Figure 1.
          
          We will now describe these structures in more detail.
          
          Image file header
          
          A TIFF  file begins  with an 8-byte image file header, containing
          the following information:
          
          Bytes 0-1:     The first  word of  the file  specifies  the  byte
          order used within the file.  Legal values are:
          
                    _II_ (hex 4949)
                    _MM_ (hex 4D4D)
          
               In the  _II_   format,  byte  order  is  always  from  least
          significant to  most significant,  for  both  16-bit  and  32-bit
          integers.   In the  _MM_   format, byte order is always from most
          significant to  least significant,  for both  16-bit  and  32-bit
          integers.   In both  formats, character  strings are  stored into
          sequential byte locations.
          
               All  TIFF   readers  should  support  both  byte  orders_see
          Appendix G.
          
          Bytes 2-3 The second  word of  the  file  is  the  TIFF  _version
          number._   This number, 42 (2A in hex), is not to be equated with
          the current  Revision of  the TIFF  specification.   In fact, the
          TIFF version  number (42)  has never  changed, and probably never









          TIFF 5.0                                          page 4          TIFF 5.0                                          page 4


          will.   If it  ever does,  it means that TIFF has changed in some
          way so  radical that  a TIFF  reader should  give up immediately.
          The number 42 was chosen for its deep philosophical significance.
          It can and should be used as additional verification that this is
          indeed a TIFF file.
          
               A TIFF  file does  not have  a real version/revision number.
          This was  an explicit,  conscious design  decision.  In many file
          formats, fields  take on different meanings depending on a single
          version number.   The  problem is that as the file format _ages,_
          it becomes  increasingly difficult  to document which fields mean
          what in  a given  version, and older software usually has to give
          up if  it encounters  a file  with a  newer version  number.   We
          wanted TIFF  fields to have a permanent and well-defined meaning,
          so that  _older_ software  can usually  read _newer_  TIFF files.
          The bottom line is lower software release costs and more reliable
          software.
          
          Bytes 4-7 This long  word contains  the offset  (in bytes) of the
          first Image File Directory.  The directory may be at any location
          in the  file after  the header but must begin on a word boundary.
          In particular,  an Image File Directory may follow the image data
          it describes.   Readers must simply follow the pointers, wherever
          they may lead.
          
               (The term  _byte offset_  is always used in this document to
          refer to  a location  with respect  to the beginning of the file.
          The first byte of the file has an offset of 0.)
          
          
          Image file directory
          
          An Image  File Directory  (IFD) consists of a 2-byte count of the
          number of  entries (i.e.,  the number  of fields),  followed by a
          sequence of 12-byte field entries, followed by a 4-byte offset of
          the next  Image File  Directory (or 0 if none).  Do not forget to
          write the 4 bytes of 0 after the last IFD.
          
          Each 12-byte IFD entry has the following format:
          
          Bytes 0-1 contain the Tag for the field.
          Bytes 2-3 contain the field Type.
          Bytes 4-7 contain the  Length (_Count_  might have  been a better
          term) of the field.
          Bytes 8-11     contain the  Value Offset,  the  file  offset  (in
          bytes) of  the Value  for the  field.   The Value  is expected to
          begin on  a word  boundary; the  corresponding Value  Offset will
          thus be  an even  number.  This file offset may point to anywhere
          in the file, including after the image data.
          
          The entries  in an  IFD must be sorted in ascending order by Tag.
          Note that this is not the order in which the fields are described
          in this  document.   For a  numerically ordered list of tags, see










          TIFF 5.0                                          page 5          TIFF 5.0                                          page 5


          Appendix E.  The Values to which directory entries point need not
          be in any particular order in the file.
          
          In order  to save time and space, the Value Offset is interpreted
          to contain  the Value  instead of  pointing to  the Value  if the
          Value fits  into 4  bytes.  If the Value is less than 4 bytes, it
          is left-justified within the 4-byte Value Offset, i.e., stored in
          the lower-numbered bytes.  Whether or not the Value fits within 4
          bytes is  determined by  looking at  the Type  and Length  of the
          field.
          
          The Length  is specified in terms of the data type, not the total
          number of bytes.  A single 16-bit word (SHORT) has a Length of 1,
          not 2,  for example.   The  data  types  and  their  lengths  are
          described below:
          
          1 = BYTE  An 8-bit unsigned integer.
          2 = ASCII 8-bit bytes  that store ASCII codes; the last byte must
          be null.
          3 = SHORT A 16-bit (2-byte) unsigned integer.
          4 = LONG  A 32-bit (4-byte) unsigned integer.
          5 = RATIONAL   Two LONG_s:  the first represents the numerator of
          a fraction, the second the denominator.
          
          The value of the Length part of an ASCII field entry includes the
          null.   If padding  is necessary, the Length does not include the
          pad byte.   Note  that there  is no  _count byte,_ as there is in
          Pascal-type strings.   The Length part of the field takes care of
          that.   The null  is not  strictly necessary, but may make things
          slightly simpler for C programmers.
          
          The reader  should check  the type  to ensure  that it is what he
          expects.   TIFF currently  allows more than 1 valid type for some
          fields.   For example,  ImageWidth and ImageLength were specified
          as having  type SHORT.  Very large images with more than 64K rows
          or columns  are possible with some devices even now.  Rather than
          add parallel  LONG tags  for these fields, it is cleaner to allow
          both SHORT  and LONG  for ImageWidth  and similar  fields.    See
          Appendix G for specific recommendations.
          
          Note that  there may  be more  than one IFD.  Each IFD is said to
          define a _subfile._   One potential use of subsequent subfiles is
          to describe  a _sub-image_   that  is somehow related to the main
          image, such as a reduced resolution version of the image.
          
          If you have not already done so, you may wish to turn to Appendix
          G to study the sample TIFF images.
          
          
          2) Definitions
          
          Note that the TIFF structure as described in the previous section
          is not  specific to  imaging applications in any way.  It is only










          TIFF 5.0                                          page 6          TIFF 5.0                                          page 6


          the definitions of the fields themselves that jointly describe an
          image.
          
          Before we  begin defining  the fields,  we will define some basic
          concepts.   An image  is defined  to be  a rectangular  array  of
          _pixels,_  each of which consists of one or more _samples._  With
          monochromatic data,  we have  one sample  per pixel, and _sample_
          and _pixel_   can  be  used  interchangeably.    RGB  color  data
          contains three samples per pixel.
          
          
          3) The Fields
          
          This section  describes the  fields defined  in this  version  of
          TIFF.   More fields  may be  added in future versions_if possible
          they will  be added in such a way so as not to break old software
          that encounters a newer TIFF file.
          
          The documentation  for each  field contains the name of the field
          (quite arbitrary, but convenient), the Tag value, the field Type,
          the Number of Values (N) expected, comments describing the field,
          and the  default, if  any.  Readers must assume the default value
          if the field does not exist.
          
          _No default_  does not  mean that  a TIFF  writer should  not pay
          attention to  the tag.  It simply means that there is no default.
          If the  writer has reason to believe that readers will care about
          the value  of this  field, the writer should write the field with
          the appropriate value.  TIFF readers can do whatever they want if
          they encounter a missing _no default_ field that they care about,
          short of  refusing to  import the file.  For example, if a writer
          does  not  write  out  a  PhotometricInterpretation  field,  some
          applications will  interpret the  image _correctly,_  and  others
          will display  the image  inverted.  This is not a good situation,
          and writers should be careful not to let it happen.
          
          The  fields   are  grouped   into  several  categories:    basic,
          informational, facsimile,  document storage and retrieval, and no
          longer recommended.   A  future version  of the specification may
          pull some of these categories into separate companion documents.
          
          Many fields  are described  in this  document, but  most are  not
          _required._   See Appendix  G for  a list  of required fields, as
          well as  examples of  how to combine fields into valid and useful
          TIFF files.
          Basic Fields
          
          
          Basic fields  are  fields  that  are  fundamental  to  the  pixel
          architecture or visual characteristics of an image.
          
          BitsPerSample
          Tag  = 258  (102)
          Type = SHORT









          TIFF 5.0                                          page 7          TIFF 5.0                                          page 7


          N    = SamplesPerPixel
          
          Number of bits per sample.  Note that this tag allows a different
          number of  bits per  sample for  each sample  corresponding to  a
          pixel.   For example, RGB color data could use a different number
          of bits  per sample for each of the three color planes.  Most RGB
          files will have the same number of BitsPerSample for each sample.
          Even in this case, be sure to include all three entries.  Writing
          _8_ when you mean _8,8,8_ sets a bad precedent for other fields.
          
          Default = 1.  See also SamplesPerPixel.
          
          
          ColorMap
          Tag  = 320 (140)
          Type = SHORT
          N    = 3 * (2**BitsPerSample)
          
          This tag  defines a  Red-Green-Blue color  map for  palette color
          images.   The palette color pixel value is used to index into all
          3 subcurves.   For  example, a Palette color pixel having a value
          of 0  would be  displayed according  to the 0th entry of the Red,
          Green, and Blue subcurves.
          
          The subcurves  are stored  sequentially.   The Red  entries  come
          first, followed  by the  Green  entries,  followed  by  the  Blue
          entries.   The length  of each  subcurve is  2**BitsPerSample.  A
          ColorMap entry  for an  8-bit Palette color image would therefore
          have 3  * 256  entries.   The width  of each entry is 16 bits, as
          implied  by  the  type  of  SHORT.    0  represents  the  minimum
          intensity, and  65535 represents the maximum intensity.  Black is
          represented by  0,0,0, and  white by  65535, 65535,  65535.   The
          purpose of  the color  map is to act as a _lookup_  table mapping
          pixel values from 0 to 2**BitsPerSample-1 into RGB triplets.
          
          The ColorResponseCurves  field may  be used  in conjunction  with
          ColorMap to further refine the meaning of the RGB triplets in the
          ColorMap.   However, the  ColorResponseCurves default  should  be
          sufficient in most cases.
          
          See also PhotometricInterpretation_palette color.
          
          No default.   ColorMap  must be  included in  all  palette  color
          images.
          
          
          ColorResponseCurves
          Tag  = 301 (12D)
          Type = SHORT
          N    = 3 * (2**BitsPerSample)
          
          This tag  defines three  color response curves, one each for Red,
          Green and  Blue color  information.   The Red entries come first,
          followed by the Green entries, followed by the Blue entries.  The









          TIFF 5.0                                          page 8          TIFF 5.0                                          page 8


          length  of   each  subcurve   is  2**BitsPerSample,   using   the
          BitsPerSample value corresponding to the respective primary.  The
          width of  each entry is 16 bits, as implied by the type of SHORT.
          0 represents  the minimum  intensity, and  65535  represents  the
          maximum intensity.   Black  is represented by 0,0,0, and white by
          65535, 65535,  65535.   Therefore, a ColorResponseCurve entry for
          RGB data  where each of the samples is 8 bits deep would have 3 *
          256 entries, each consisting of a SHORT.
          
          The purpose of the color response curves is to refine the content
          of RGB color images.
          
          See Appendix H, section VII, for further information.
          
          Default:  curves based on the NTSC recommended gamma of 2.2.
          
          
          Compression
          Tag  = 259  (103)
          Type = SHORT
          N    = 1
          
          1 =  No compression,  but pack  data into  bytes  as  tightly  as
          possible, with  no unused  bits except  at the end of a row.  The
          bytes are  stored as  an array of type BYTE, for BitsPerSample <=
          8,  SHORT   if  BitsPerSample   >  8  and  <=  16,  and  LONG  if
          BitsPerSample >  16 and <= 32.  The byte ordering of data >8 bits
          must be  consistent with  that specified  in the TIFF file header
          (bytes 0  and 1).   _II_    format  files  will  have  the  least
          significant bytes  preceeding the  most significant  bytes  while
          _MM_  format files will have the opposite.
          
               If the  number of  bits per  sample is not a power of 2, and
          you are willing to give up some space for better performance, you
          may wish to use the next higher power of 2.  For example, if your
          data can  be represented  in 6 bits, you may wish to specify that
          it is 8 bits deep.
          
               Rows are  required to  begin on byte boundaries.  The number
          of bytes  per row  is therefore  (ImageWidth *  SamplesPerPixel *
          BitsPerSample  +   7)  /  8,  assuming  integer  arithmetic,  for
          PlanarConfiguration=1.     Bytes  per   row  is   (ImageWidth   *
          BitsPerSample + 7) / 8 for PlanarConfiguration=2.
          
               Some graphics  systems want rows to be word- or double-word-
          aligned.   Uncompressed TIFF  rows will  need to  be copied  into
          word- or  double-word-padded row  buffers before  being passed to
          the graphics routines in these environments.
          
          2 =  CCITT Group  3 1-Dimensional  Modified  Huffman  run  length
          encoding.   See Appendix  B:   _Data Compression  --  Scheme  2._
          BitsPerSample must  be 1,  since  this  type  of  compression  is
          defined only for bilevel images.
          









          TIFF 5.0                                          page 9          TIFF 5.0                                          page 9


               When  you  decompress  data  that  has  been  compressed  by
          Compression=2, you  must translate  white runs into 0_s and black
          runs into  1_s.   Therefore, the normal PhotometricInterpretation
          for those  compression types  is 0  (WhiteIsZero).   If a  reader
          encounters a  PhotometricInterpretation of  1  (BlackIsZero)  for
          such an  image, the  image should  be displayed  and printed with
          black and white reversed.
          
          5 = LZW Compression,  for grayscale, mapped color, and full color
          images.  See Appendix F.
          
          32773 =  PackBits compression,  a simple byte oriented run length
          scheme for 1-bit images.  See Appendix C.
          
          Data compression only applies to raster image data, as pointed to
          by StripOffsets.  All other TIFF information is unaffected.
          
          Default = 1.
          
          
          GrayResponseCurve
          Tag  = 291 (123)
          Type = SHORT
          N    = 2**BitsPerSample
          
          The purpose  of the  gray response curve and the gray units is to
          provide more  exact photometric  interpretation  information  for
          gray scale image data, in terms of optical density.
          
          The  GrayScaleResponseUnits   specifies  the   accuracy  of   the
          information contained  in the  curve.   Since optical  density is
          specified in  terms of  fractional numbers, this tag is necessary
          to know  how to  interpret the  stored integer  information.  For
          example, if  GrayScaleResponseUnits is  set to 4 (ten-thousandths
          of a  unit), and a GrayScaleResponseCurve number for gray level 4
          is 3455,  then the  resulting actual  value is  0.3455.   Optical
          densitometers typically measure densities within the range of 0.0
          to 2.0.
          
          If the  gray scale  response curve  is known  for the data in the
          TIFF file, and if the gray scale response of the output device is
          known, then  an intelligent  conversion can  be made  between the
          input data and the output device.  For example, the output can be
          made to  look just  like the  input.   In addition,  if the input
          image lacks  contrast (as  can be  seen from the response curve),
          then appropriate contrast enhancements can be made.
          
          The purpose  of the  gray scale  response curve  is to  act as  a
          _lookup_   table mapping values from 0 to 2**BitsPerSample-1 into
          specific   density    values.      The   0th   element   of   the
          GrayResponseCurve array  is used to define the gray value for all
          pixels  having   a  value   of  0,   the  1st   element  of   the
          GrayResponseCurve array  is used to define the gray value for all
          pixels having  a value of 1, and so on, up to 2**BitsPerSample-1.









          TIFF 5.0                                          page 10          TIFF 5.0                                          page 10


          If your  data is  _really,_ say, 7-bit data, but you are adding a
          1-bit pad  to each  pixel to  turn it into 8-bit data, everything
          still works:   If  the data is high-order justified, half of your
          GrayResponseCurve entries  (the odd ones, probably) will never be
          used, but  that doesn_t  hurt anything.  If the data is low-order
          justified, your  pixel values  will be between 0 and 127, so make
          your GrayResponseCurve  accordingly.   What your  curve does from
          128 to  255 doesn’t matter.  Note that low-order justification is
          probably not  a good  idea, however,  since not  all applications
          look at GrayResponseCurve.  Note also that LZW compression yields
          the same  compression ratio  regardless of  whether the  data  is
          high-order or low-order justified.
          
          It is  permissable to  have a  GrayResponseCurve even for bilevel
          (1-bit) images.   The  GrayResponseCurve will  have 2 values.  It
          should be noted, however, that TIFF B readers are not required to
          pay attention  to  GrayResponseCurves  in  TIFF  B  files.    See
          Appendix G.
          
          If both  GrayResponseCurve and  PhotometricInterpretation  fields
          exist  in   the  IFD,   GrayResponseCurve  values   override  the
          PhotometricInterpretation value.   But it is a good idea to write
          out both, since some applications do not yet pay attention to the
          GrayResponseCurve.
          
          Writers may  wish to  purchase a  Kodak Reflection Density Guide,
          catalog number  146 5947,  available for  $10 or  so at  prepress
          supply houses,  to help them figure out reasonable density values
          for their scanner or frame grabber.  If that sounds like too much
          work,   we    recommend   a    curve   that    is    linear    in
          intensity/reflectance.  To compute reflectance from density:  R =
          1 /  pow(10,D).   To compute  density from reflectance: D = log10
          (1/R).   A typical  4-bit GrayResponseCurve  may  look  therefore
          something like:   2000,  1177, 875, 699, 574, 477, 398, 331, 273,
          222, 176,  135, 97, 62, 30, 0, assuming GrayResponseUnit=3.  Such
          a curve would be consistent with PhotometricInterpretation=1.
          
          See also GrayResponseUnit, PhotometricInterpretation, ColorMap.
          
          
          GrayResponseUnit
          Tag  = 290 (122)
          Type = SHORT
          N    = 1
          
          1 = Number represents tenths of a unit.
          2 = Number represents hundredths of a unit.
          3 = Number represents thousandths of a unit.
          4 = Number represents ten-thousandths of a unit.
          5 = Number represents hundred-thousandths of a unit.
          
          Modifies GrayResponseCurve.
          
          See also GrayResponseCurve.









          TIFF 5.0                                          page 11          TIFF 5.0                                          page 11


          
          For historical  reasons, the  default is 2.  However, for greater
          accuracy, we recommend using 3.
          
          
          ImageLength
          Tag  = 257  (101)
          Type = SHORT or LONG
          N    = 1
          
          The image_s  length (height) in pixels (Y: vertical).  The number
          of rows  (sometimes described as _scan lines") in the image.  See
          also ImageWidth.
          
          No default.
          
          
          ImageWidth
          Tag  = 256  (100)
          Type = SHORT or LONG
          N    = 1
          
          The image_s  width, in  pixels (X:  horizontal).   The number  of
          columns in the image.  See also ImageLength.
          
          No default.
          
          
          NewSubfileType
          Tag =  254  (FE)
          Type = LONG
          N = 1
          
          Replaces the  old SubfileType  field, due  to limitations  in the
          definition of that field.
          
          A general  indication of  the kind  of data  that is contained in
          this subfile.   This  field is  made up of a set of 32 flag bits.
          Unused bits are expected to be 0.  Bit 0 is the low-order bit.
          
          Currently defined values are:
          
          Bit 0     is 1  if the  image is  a reduced resolution version of
          another image in this TIFF file; else the bit is 0.
          Bit 1     is 1  if the  image is  a single  page of  a multi-page
          image (see the PageNumber tag description); else the bit is 0.
          Bit 2     is 1  if the  image defines  a  transparency  mask  for
          another image  in this  TIFF file.  The PhotometricInterpretation
          value must be 4, designating a transparency mask.
          
          These values  have been  defined as  bit flags  because they  are
          pretty much independent of each other.  For example, it be useful
          to have  four images  in a  single TIFF  file: a  full resolution
          image, a  reduced resolution  image, a  transparency mask for the









          TIFF 5.0                                          page 12          TIFF 5.0                                          page 12


          full resolution  image, and  a transparency  mask for the reduced
          resolution image.  Each of the four images would have a different
          value for the NewSubfileType field.
          
          Default is 0.
          
          
          PhotometricInterpretation
          Tag  = 262  (106)
          Type = SHORT
          N    = 1
          
          0 =  For bilevel  and grayscale  images:   0 is  imaged as white.
          2**BitsPerSample-1 is  imaged as  black.    If  GrayResponseCurve
          exists,  it   overrides  the   PhotometricInterpretation   value,
          although  it  is  safer  to  make  them  match,  since  some  old
          applications may still be ignoring GrayResponseCurve. This is the
          normal value for Compression=2.
          
          1 =  For bilevel  and grayscale  images:   0 is  imaged as black.
          2**BitsPerSample-1  is  imaged  as  white.  If  GrayResponseCurve
          exists,  it   overrides  the   PhotometricInterpretation   value,
          although  it  is  safer  to  make  them  match,  since  some  old
          applications may  still be  ignoring GrayResponseCurve.  If  this
          value is  specified for  Compression=2, the  image should display
          and print reversed.
          
          2 = RGB.  In the RGB model, a color is described as a combination
          of the  three primary  colors of  light (red, green, and blue) in
          particular concentrations.   For  each of  the three  samples,  0
          represents minimum intensity, and 2**BitsPerSample - 1 represents
          maximum intensity.   Thus  an RGB  value  of  (0,0,0)  represents
          black,  and   (255,255,255)  represents   white,  assuming  8-bit
          samples.   For PlanarConfiguration = 1, the samples are stored in
          the indicated  order:   first Red,  then Green,  then Blue.   For
          PlanarConfiguration =  2, the  StripOffsets for the sample planes
          are stored  in the  indicated order:   first the Red sample plane
          StripOffsets, then  the Green  plane StripOffsets,  then the Blue
          plane StripOffsets.
          
               The ColorResponseCurves field may be used to globally refine
          or alter  the color  balance of  an RGB  image without  having to
          change the values of the pixels themselves.
          
          3="Palette color._     In this  mode, a color is described with a
          single sample.   The  sample is  used as  an index into ColorMap.
          The sample  is used to index into each of the red, green and blue
          curve tables to retrieve an RGB triplet defining an actual color.
          When this  PhotometricInterpretation value  is  used,  the  color
          response curves  must also  be supplied.  SamplesPerPixel must be
          1.
          
          4 =  Transparency Mask.   This  means that  the image  is used to
          define an  irregularly shaped region of another image in the same









          TIFF 5.0                                          page 13          TIFF 5.0                                          page 13


          TIFF  file.     SamplesPerPixel  and  BitsPerSample  must  be  1.
          PackBits compression  is recommended.    The  1-bits  define  the
          interior of  the region;  the 0-bits  define the  exterior of the
          region.  The Transparency Mask must have the same ImageLength and
          ImageWidth as the main image.
          
               A reader  application can  use the  mask to  determine which
          parts of the image to display.  Main image pixels that correspond
          to 1-bits  in the  transparency mask  are imaged to the screen or
          printer, but  main image  pixels that correspond to 0-bits in the
          mask are not displayed or printed.
          
               It is  possible to  generalize the  notion of a transparency
          mask to  include partial  transparency, but  it is not clear that
          such information would be useful to a desktop publishing program.
          
          No default.   That  means that  if you  care  if  your  image  is
          displayed and  printed as  _normal_ vs _inverted,_ you must write
          out this  field.   Do not rely on applications defaulting to what
          you want!   PhotometricInterpretation  =  1  is  recommended  for
          bilevel (except  for Compression=2)  and grayscale images, due to
          popular user  interfaces for changing the brightness and contrast
          of images.
          
          
          PlanarConfiguration
          Tag  = 284  (11C)
          Type = SHORT
          N    = 1
          
          1 =  The sample values for each pixel are stored contiguously, so
          that   there    is   a    single   image    plane.            See
          PhotometricInterpretation to  determine the  order of the samples
          within the  pixel data.   So,  for RGB  data, the  data is stored
          RGBRGBRGB...and so on.
          
          2 =  The samples  are stored  in separate  _sample planes._   The
          values in StripOffsets and StripByteCounts are then arranged as a
          2-dimensional array, with SamplesPerPixel rows and StripsPerImage
          columns.      (All of  the columns  for row  0 are  stored first,
          followed   by    the   columns    of   row   1,   and   so   on.)
          PhotometricInterpretation describes  the type  of  data  that  is
          stored in  each sample  plane.   For example,  RGB data is stored
          with the  Red samples  in one sample plane, the Green in another,
          and the Blue in another.
          
          If SamplesPerPixel  is 1,  PlanarConfiguration is irrelevant, and
          should not be included.
          Default is 1.  See also BitsPerSample, SamplesPerPixel.
          
          
          Predictor
          Tag  = 317 (13D)
          Type = SHORT









          TIFF 5.0                                          page 14          TIFF 5.0                                          page 14


          N    = 1
          
          To be used when Compression=5 (LZW).  See Appendix F.
          
          1 = No prediction scheme used before coding.
          
          Default is 1.
          
          
          ResolutionUnit
          Tag  = 296 (128)
          Type = SHORT
          N    = 1
          
          To be used with XResolution and YResolution.
          
          1 =  No absolute  unit of  measurement.  Used for images that may
          have a  non-square  aspect  ratio,  but  no  meaningful  absolute
          dimensions.   The drawback  of ResolutionUnit=1 is that different
          applications will  import the  image at different sizes.  Even if
          the decision  is quite  arbitrary, it might be better to use dots
          per inch  or  dots  per  centimeter,  and  pick  XResolution  and
          YResolution such that the aspect ratio is correct and the maximum
          dimension of  the image is about four inches (the _four_ is quite
          arbitrary.)
          2 = Inch.
          3 = Centimeter.
          
          Default is 2.  See also XResolution, YResolution.
          
          
          RowsPerStrip
          Tag  = 278  (116)
          Type = SHORT or LONG
          N    = 1
          
          The number  of rows  per strip.  The image data is organized into
          strips for  fast access  to individual  rows  when  the  data  is
          compressed_though this  field is  valid even  if the  data is not
          compressed.
          
          RowsPerStrip and  ImageLength together  tell  us  the  number  of
          strips in  the entire  image.   The equation  is StripsPerImage =
          (ImageLength + RowsPerStrip - 1) / RowsPerStrip, assuming integer
          arithmetic.
          
          Note that  either SHORT  or LONG  values can  be used  to specify
          RowsPerStrip.   SHORT values  may be  used for  small TIFF files.
          It should  be noted,  however, that  earlier  TIFF  specification
          revisions required  LONG values  and that  some software  may not
          expect SHORT values.  See Appendix G for further recommendations.
          
          Default is  2**32 -  1, which  is effectively infinity.  That is,
          the entire  image is  one strip.   We  do not  recommend a single









          TIFF 5.0                                          page 15          TIFF 5.0                                          page 15


          strip, however.   Choose  RowsPerStrip such  that each  strip  is
          about 8K  bytes, even  if the  data is  not compressed,  since it
          makes buffering  simpler for  readers.   The _8K_  part is pretty
          arbitrary, but seems to work well.
          
          See also ImageLength, StripOffsets, StripByteCounts.
          
          
          SamplesPerPixel
          Tag  = 277  (115)
          Type = SHORT
          N    = 1
          
          The number  of samples  per pixel.    SamplesPerPixel  is  1  for
          bilevel, grayscale, and palette color images.  SamplesPerPixel is
          3 for RGB images.
          
          Default = 1.  See also BitsPerSample, PhotometricInterpretation.
          
          
          StripByteCounts
          Tag  = 279  (117)
          Type = SHORT or LONG
          N    = StripsPerImage for PlanarConfiguration equal to 1.
               = SamplesPerPixel  * StripsPerImage  for PlanarConfiguration
          equal to 2
          
          For each strip, the number of bytes in that strip.  The existence
          of  this   field  greatly   simplifies  the  chore  of  buffering
          compressed data, if the strip size is reasonable.
          
          No default.  See also StripOffsets, RowsPerStrip.
          
          
          StripOffsets
          Tag  = 273  (111)
          Type = SHORT or LONG
          N    = StripsPerImage for PlanarConfiguration equal to 1.
               = SamplesPerPixel  * StripsPerImage  for PlanarConfiguration
          equal to 2
          
          For each  strip, the  byte offset  of that  strip.  The offset is
          specified with  respect to  the beginning of the TIFF file.  Note
          that this  implies that  each strip has a location independent of
          the locations  of other  strips.   This feature may be useful for
          editing applications.  This field is the only way for a reader to
          find the image data, and hence must exist.
          
          Note that  either SHORT or LONG values can be used to specify the
          strip offsets.   SHORT  values  may be used for small TIFF files.
          It should  be noted,  however, that  earlier TIFF  specifications
          required LONG strip offsets and that some software may not expect
          SHORT values.  See Appendix G for further recommendations.
          









          TIFF 5.0                                          page 16          TIFF 5.0                                          page 16


          No default.  See also StripByteCounts, RowsPerStrip.
          
          
          XResolution
          Tag  = 282  (11A)
          Type = RATIONAL
          N    = 1
          
          The number of pixels per ResolutionUnit in the X direction, i.e.,
          in the  ImageWidth direction.   It  is, of  course, not mandatory
          that the  image be  actually printed  at the size implied by this
          parameter.   It is  up to the application to use this information
          as it wishes.
          
          No default.  See also YResolution, ResolutionUnit.
          
          
          YResolution
          Tag  = 283  (11B)
          Type = RATIONAL
          N    = 1
          
          The number of pixels per ResolutionUnit in the Y direction, i.e.,
          in the ImageLength direction.
          
          No default.  See also XResolution, ResolutionUnit.
          
          
          Informational Fields
          
          
          Informational  fields   are  fields   that  can   provide  useful
          information to  a user,  such as where the image came from.  Most
          are ASCII  fields.   An application could have some sort of _More
          Info..._ dialog box to display such information.
          
          Artist
          Tag  = 315  (13B)
          Type = ASCII
          
          Person who created the image.
          
          If you need to attach a Copyright notice to an image, this is the
          place to  do it.  In fact, you may wish to write out the contents
          of the field immediately after the 8-byte TIFF header.  Just make
          sure your  IFD and field pointers are set accordingly, and you_re
          all set.
          
          
          DateTime
          Tag  = 306  (132)
          Type = ASCII
          N    = 20
          









          TIFF 5.0                                          page 17          TIFF 5.0                                          page 17


          Date and  time of  image creation.   Use  the format  _YYYY:MM:DD
          HH:MM:SS_, with hours on a 24-hour clock, and one space character
          between the  date and  the time.    The  length  of  the  string,
          including the null, is 20 bytes.
          
          
          HostComputer
          Tag  = 316  (13C)
          Type = ASCII
          
          _ENIAC_, or whatever.
          
          See also Make, Model, Software.
          
          
          ImageDescription
          Tag  = 270 (10E)
          Type = ASCII
          
          For example,  a user  may wish  to attach a comment such as _1988
          company picnic_ to an image.
          
          It has  been suggested  that  this  is  what  the  newspaper  and
          magazine industry calls a _slug._
          
          
          Make
          Tag  = 271  (10F)
          Type = ASCII
          
          Manufacturer of the scanner, video digitizer, or whatever.
          
          See also Model, Software.
          
          
          Model
          Tag  = 272  (110)
          Type = ASCII
          
          The  model  name/number  of  the  scanner,  video  digitizer,  or
          whatever.
          
          This tag is intended for user information only.
          
          See also Make, Software.
          
          
          Software
          Tag  = 305  (131)
          Type = ASCII
          
          Name and  release number of the software package that created the
          image.
          









          TIFF 5.0                                          page 18          TIFF 5.0                                          page 18


          This tag is intended for user information only.
          
          See also Make, Model.
          
          
          Facsimile Fields
          
          
          Facsimile fields  may be  useful if  you are  using TIFF to store
          facsimile messages  in _raw_  form.  They are not recommended for
          use in interchange with desktop publishing applications.
          
          Compression (a basic tag)
          Tag  = 259  (103)
          Type = SHORT
          N    = 1
          
          3 =  Facsimile-compatible CCITT  Group 3, exactly as specified in
          _Standardization of  Group 3  facsimile  apparatus  for  document
          transmission,_   Recommendation T.4,  Volume VII, Fascicle VII.3,
          Terminal Equipment  and Protocols  for  Telematic  Services,  The
          International  Telegraph  and  Telephone  Consultative  Committee
          (CCITT), Geneva,  1985, pages  16 through  31.   Each strip  must
          begin on  a byte  boundary.   (But recall  that an image can be a
          single strip.)   Rows  that are  not the first row of a strip are
          not required  to begin on a byte boundary.  The data is stored as
          bytes,  not   words_byte-reversal  is   not  allowed.    See  the
          Group3Options field for Group 3 options such as 1D vs 2D coding.
          
          4 =  Facsimile-compatible CCITT  Group 4, exactly as specified in
          _Facsimile Coding  Schemes and Coding Control Functions for Group
          4 Facsimile Apparatus,_  Recommendation T.6, Volume VII, Fascicle
          VII.3, Terminal  Equipment and  Protocols for Telematic Services,
          The International  Telegraph and Telephone Consultative Committee
          (CCITT), Geneva,  1985, pages  40 through  48.   Each strip  must
          begin on  a byte  boundary.  Rows that are not the first row of a
          strip are  not required to begin on a byte boundary.  The data is
          stored as  bytes, not  words.   See the  Group4Options field  for
          Group 4 options.
          
          
          Group3Options
          Tag  = 292  (124)
          Type = LONG
          N    = 1
          
          See Compression=3.   This  field is  made up  of a set of 32 flag
          bits.   Unused bits are expected to be 0.  Bit 0 is the low-order
          bit.   It is probably not safe to try to read the file if any bit
          of this field is set that you don_t know the meaning of.
          
          Bit 0     is 1  for 2-dimensional  coding (else  1-dimensional is
          assumed).   For 2-D  coding, if more than one strip is specified,
          each strip  must begin  with a  1-dimensionally coded line.  That









          TIFF 5.0                                          page 19          TIFF 5.0                                          page 19


          is, RowsPerStrip  should be  a multiple  of  _Parameter  K_    as
          documented in the CCITT specification.
          
          Bit 1     is 1 if uncompressed mode is used.
          
          Bit 2     is 1  if fill  bits have been added as necessary before
          EOL codes  such that  EOL always  ends on  a byte  boundary, thus
          ensuring an  eol-sequence of  a 1 byte preceded by a zero nibble:
          xxxx-0000 0000-0001.
          
          Default  is   0,  for  basic  1-dimensional  coding.    See  also
          Compression.
          
          
          Group4Options
          Tag  =  293  (125)
          Type = LONG
          N    = 1
          
          See Compression=4.   This  field is  made up  of a set of 32 flag
          bits.   Unused bits are expected to be 0.  Bit 0 is the low-order
          bit.   It is probably not safe to try to read the file if any bit
          of this  field is  set that  you don_t know the meaning of.  Gray
          scale and color coding schemes are under study, and will be added
          when finalized.
          
          For 2-D  coding, each  strip is  encoded as if it were a separate
          image.   In particular, each strip begins on a byte boundary; and
          the coding  for the first row of a strip is encoded independently
          of the  previous row,  using horizontal codes, as if the previous
          row is  entirely white.   Each strip ends with the 24-bit end-of-
          facsimile block (EOFB).
          
          Bit 0     is unused.
          Bit 1     is 1 if uncompressed mode is used.
          
          Default is  0, for  basic 2-dimensional  binary compression.  See
          also Compression.
          
          
          Document Storage and Retrieval Fields
          
          
          These fields  may be  useful for  document storage  and retrieval
          applications.   They are  not recommended  for use in interchange
          with desktop publishing applications.
          
          DocumentName
          Tag  = 269  (10D)
          Type = ASCII
          
          The name of the document from which this image was scanned.
          
          See also PageName.









          TIFF 5.0                                          page 20          TIFF 5.0                                          page 20


          
          
          PageName
          Tag  = 285  (11D)
          Type = ASCII
          
          The name of the page from which this image was scanned.
          
          See also DocumentName.
          
          No default.
          
          PageNumber
          Tag  = 297  (129)
          Type = SHORT
          N    = 2
          
          This tag is used to specify page numbers of a multiple page (e.g.
          facsimile) document.   Two SHORT values are specified.  The first
          value is the page number; the second value is the total number of
          pages in the document.
          
          Note that  pages need  not appear  in numerical order.  The first
          page is 0 (zero).
          
          No default.
          
          
          XPosition
          Tag  = 286  (11E)
          Type = RATIONAL
          
          The X  offset of  the left side of the image, with respect to the
          left side of the page, in ResolutionUnits.
          
          No default.  See also YPosition.
          
          
          YPosition
          Tag  = 287  (11F)
          Type = RATIONAL
          
          The Y  offset of the top of the image, with respect to the top of
          the page, in ResolutionUnits.  In the TIFF coordinate scheme, the
          positive Y  direction  is  down,  so  that  YPosition  is  always
          positive.
          
          No default.  See also XPosition.
          
          
          No Longer Recommended
          
          










          TIFF 5.0                                          page 21          TIFF 5.0                                          page 21


          These fields  are not  recommended except  perhaps for local use.
          They should  not be used for image interchange.  They have either
          been superseded  by other fields, have been found to have serious
          drawbacks, or are simply not as useful as once thought.  They may
          be dropped entirely from a future revision of the specification.
          
          CellLength
          Tag  = 265  (109)
          Type = SHORT
          N    = 1
          
          The length, in 1-bit samples, of the dithering/halftoning matrix.
          Assumes that Threshholding = 2.
          
          This field,  plus CellWidth  and Threshholding,  are  problematic
          because they  cannot safely be used to reverse-engineer grayscale
          image data  out of dithered/halftoned black-and-white data, which
          is their  only plausible  purpose.  The only _right_ way to do it
          is to  not bother  with anything  like these  fields, and instead
          write  some  sophisticated  pattern-matching  software  that  can
          handle screen  angles that  are not  multiples of 45 degrees, and
          other such challenging dithered/halftoned data.
          
          So we  do not  recommend trying  to convert dithered or halftoned
          data into  grayscale data.   Dithered  and halftoned data require
          careful treatment  to avoid  _stretch marks,_ but it can be done.
          If you  want grayscale images, get them directly from the scanner
          or frame grabber or whatever.
          
          No default.  See also Threshholding.
          
          
          CellWidth
          Tag  = 264  (108)
          Type = SHORT
          N    = 1
          
          The width, in 1-bit samples, of the dithering/halftoning matrix.
          
          No default.   See  also Threshholding.    See  the  comments  for
          CellLength.
          
          
          FillOrder
          Tag  = 266  (10A)
          Type = SHORT
          N    = 1
          
          The order of data values within a byte.
          1 = most significant bits of the byte are filled first.  That is,
          data values  (or code  words) are  ordered from high order bit to
          low order bit within a byte.
          2 =  least significant  bits are  filled  first.    Since  little
          interest has  been expressed  in least-significant  fill order to









          TIFF 5.0                                          page 22          TIFF 5.0                                          page 22


          date, and since it is easy and inexpensive for writers to reverse
          bit order (use a 256-byte lookup table), we recommend FillOrder=2
          for private (non-interchange) use only.
          
          Default is FillOrder = 1.
          
          
          FreeByteCounts
          Tag  = 289  (121)
          Type = LONG
          
          For each  _free block_   in  the file, the number of bytes in the
          block.
          
          TIFF  readers   can  ignore  FreeOffsets  and  FreeByteCounts  if
          present.
          
          FreeOffsets and  FreeByteCounts do  not constitute a remapping of
          the logical address space of the file.
          
          Since this  information can  be generated  by scanning  the IFDs,
          StripOffsets, and StripByteCounts, FreeByteCounts and FreeOffsets
          are not needed.
          
          In addition, it is not clear what should happen if FreeByteCounts
          and FreeOffsets exist in more than one IFD.
          
          See also FreeOffsets.
          
          
          FreeOffsets
          Tag  = 288  (120)
          Type = LONG
          
          For each _free block_  in the file, its byte offset.
          
          See also FreeByteCounts.
          
          
          MaxSampleValue
          Tag  = 281  (119)
          Type = SHORT
          N    = SamplesPerPixel
          
          The maximum  used sample  value.    For  example,  if  the  image
          consists of  6-bit data  low-order-justified  into  8-bit  bytes,
          MaxSampleValue will  be no  greater than 63. This is field is not
          to be  used to  affect the  visual appearance  of the  image when
          displayed.   Nor should  the values  of  this  field  affect  the
          interpretation of  any other  field.    Use  it  for  statistical
          purposes only.
          
          Default is 2**(BitsPerSample) - 1.
          









          TIFF 5.0                                          page 23          TIFF 5.0                                          page 23


          
          MinSampleValue
          Tag  = 280  (118)
          Type = SHORT
          N    = SamplesPerPixel
          
          The minimum  used sample  value.  This field is not to be used to
          affect the  visual appearance  of the  image when displayed.  See
          the comments for MaxSampleValue.
          
          Default is 0.
          
          
          SubfileType
          Tag  = 255  (FF)
          Type = SHORT
          N    = 1
          
          A general  indication of  the kind  of data  that is contained in
          this subfile.  Currently defined values are:
          
          1 =  full  resolution  image  data_ImageWidth,  ImageLength,  and
          StripOffsets are required fields; and
          2 =  reduced resolution  image data_ImageWidth,  ImageLength, and
          StripOffsets are  required fields.   It is further assumed that a
          reduced resolution  image is  a reduced  version  of  the  entire
          extent of the corresponding full resolution data.
          3 =  single page  of a  multi-page image  (see the PageNumber tag
          description).
          
          Note that several image types can be found in a single TIFF file,
          with each subfile described by its own IFD.
          
          No default.
          
          Continued use  of this  field is not recommended.  Writers should
          instead use the new and more general NewSubfileType field.
          
          
          Orientation
          Tag  = 274 (112)
          Type = SHORT
          N    = 1
          
          1 =  The 0th  row represents the visual top of the image, and the
          0th column represents the visual left hand side.
          2 =  The 0th  row represents the visual top of the image, and the
          0th column represents the visual right hand side.
          3 =  The 0th  row represents  the visual bottom of the image, and
          the 0th column represents the visual right hand side.
          4 =  The 0th  row represents  the visual bottom of the image, and
          the 0th column represents the visual left hand side.
          5 =  The 0th  row represents  the visual  left hand  side of  the
          image, and the 0th column represents the visual top.









          TIFF 5.0                                          page 24          TIFF 5.0                                          page 24


          6 =  The 0th  row represents  the visual  right hand  side of the
          image, and the 0th column represents the visual top.
          7 =  The 0th  row represents  the visual  right hand  side of the
          image, and the 0th column represents the visual bottom.
          8 =  The 0th  row represents  the visual  left hand  side of  the
          image, and the 0th column represents the visual bottom.
          
          Default is 1.
          
          This field is recommended for private (non-interchange) use only.
          It is extremely costly for most readers to perform image rotation
          _on the  fly,_ i.e.,  when importing  and printing;  and users of
          most  desktop  publishing  applications  do  not  expect  a  file
          imported by the application to be altered permanently in any way.
          
          
          Threshholding
          Tag  = 263  (107)
          Type = SHORT
          N    = 1
          
          1 = a bilevel _line art_  scan.  BitsPerSample must be 1.
          2 =  a _dithered_   scan, usually of continuous tone data such as
          photographs. BitsPerSample must be 1.
          3 = Error Diffused.
          
          Default is Threshholding = 1.  See also CellWidth, CellLength.
          4) Private Fields
          
          An organization  may wish to store information that is meaningful
          to only that organization in a TIFF file.  Tags numbered 32768 or
          higher  are  reserved  for  that  purpose.    Upon  request,  the
          administrator will  allocate and register a block of private tags
          for an  organization, to  avoid  possible  conflicts  with  other
          organizations.   Tags are  normally allocated  in blocks of five.
          If that is not enough, feel free to ask for more. You do not need
          to tell  the TIFF administrator or anyone else what you are going
          to use them for.
          
          Private enumerated  values  can  be  accommodated  in  a  similar
          fashion.   For example,  you may  wish to  experiment with  a new
          compression scheme  within TIFF.   Enumeration constants numbered
          32768 or  higher are  reserved for  private usage.  Upon request,
          the  administrator   will  allocate   and  register  a  block  of
          enumerated values  for a  particular field  (Compression, in  our
          example), to avoid possible conflicts.
          
          Tags and  values which  are allocated in the private number range
          are not  prohibited from  being included  in a future revision of
          this specification.   Several  such instances can be found in the
          TIFF specification.
          
          Do not  choose your  own tag  numbers.  If you do, it could cause
          serious problems some day.









          TIFF 5.0                                          page 25          TIFF 5.0                                          page 25


          
          
          5) Image File Format Issues
          
          In the  quest to  give users no reason NOT to buy a product, some
          scanning and  image editing  applications overwhelm users with an
          incredible number  of _Save  As..._ options.  Let_s get rid of as
          many of  these as  we possibly  can.   For example, a single TIFF
          choice should  suffice once most major readers are supporting the
          three TIFF compression schemes; then writers can always compress.
          And given  TIFF_s flexibility,  including private  tag and  image
          editing  support   features,  there  does  not  seem  to  be  any
          legitimate reason  for continuing  to  write  image  files  using
          proprietary formats.
          
          Along the  same lines,  there is no excuse for making a user have
          to know  the file  format of  a file  that is  to be  read by  an
          application program.   TIFF  files, as  well as  most other  file
          formats, contain  sufficient information  to enable  software  to
          automatically and  reliably distinguish  one type  of  file  from
          another.
          
          
          6) For Further Information
          
          Contact the  Aldus Developers_ Desk for sample TIFF files, source
          code fragments,  and  a  list  of  features  that  are  currently
          supported in  Aldus products.   The Aldus Developers_ Desk is the
          current _TIFF administrator._
          
          Various TIFF  related  aids  are  found  in  Microsoft_s  Windows
          Developers Tookit for developers writing Windows applications.
          
          Finally, a  number of  scanner vendors are providing various TIFF
          services, such  as helping  to distribute  the TIFF specification
          and answering  TIFF questions.   Contact  the appropriate product
          manager or developer support service group.
          

























          TIFF 5.0                                          page 26          TIFF 5.0                                          page 26


          Appendix A:  Tag Structure Rationale
          
          
          A file  format is  defined by  both form (structure) and content.
          The content of TIFF consists of definitions of individual fields.
          It is therefore the content that we are ultimately interested in.
          The structure  merely tells  us how  to find the fields.  Yet the
          structure deserves  serious consideration for a number of reasons
          that are not at all obvious at first glance.  Since the structure
          described  herein   departs  significantly   from  several  other
          approaches, it may be useful to discuss the rationale behind it.
          
          The simplest,  most straightforward  structure for something like
          an image  file is  a positional  format.  In a positional scheme,
          the location  of the  data defines  what the  data  means.    For
          example, the  field for  _number of  rows_ might  begin  at  byte
          offset 30 in the image file.
          
          This approach  is simple and easy to implement and is perfect for
          static environments.   But  if a  significant amount  of  ongoing
          change must  be accommodated,  subtle problems  begin to  appear.
          For example,  suppose that  a field  must be superseded by a new,
          more general  field.  You could bump a version number to flag the
          change.   Then  new  software  has  no  problem  doing  something
          sensible with  old data, and all old software will reject the new
          data, even  software that  didn_t care about the old field.  This
          may seem like no more than a minor annoyance at first glance, but
          causing old  software to  break more  often than  it would really
          need to  can be very costly and, inevitably, causes much gnashing
          of teeth among customers.
          
          Furthermore, it  can be  avoided.   One approach  is to  store  a
          _valid_ flag  bit for each field.  Now you don_t have to bump the
          version number,  as long  as you  can put the new field somewhere
          that doesn_t  disturb any  of the  old fields.  Old software that
          didn_t care about that old field anyway can continue to function.
          (Old software  that did  care will of course have to give up, but
          this is an unavoidable price to be paid for the sake of progress,
          barring total omniscience.)
          
          Another problem  that crops  up frequently is that certain fields
          are likely  to make  sense only  if  other  fields  have  certain
          values.   This is not such a serious problem in practice; it just
          makes things  more confusing.   Nevertheless,  we note  that  the
          _valid_ flag bits described in the previous paragraph can help to
          clarify the situation.
          
          Field-dumping  programs   can  be  very  helpful  for  diagnostic
          purposes.   A desirable  characteristic of such a program is that
          it doesn_t  have to  know much  about what  it is  dumping.    In
          particular, it would be nice if the program could dump ASCII data
          in ASCII  format, integer  data in  integer format,  and  so  on,
          without having  to teach  the program  about new  fields all  the
          time.   So maybe  we should  add a  _data type_  component to our









          TIFF 5.0                                          page 27          TIFF 5.0                                          page 27


          fields, plus  information on  how long  the field is, so that our
          dump program can walk through the fields without knowing what the
          fields _mean."
          
          But note  that if we add one more component to each field, namely
          a tag  that tells  what the field means, we can dispense with the
          _valid_ flag  bits, and  we can  also avoid  wasting space on the
          non-valid fields in the file.  Simple image creation applications
          can write out several fields and be done.
          
          We have  now derived  the essentials  of a  tag-based image  file
          format.
          
          Finally, a  caveat.  A tag based scheme cannot guarantee painless
          growth.   But is  does provide  a useful  tool to  assist in  the
          process.
          














































          TIFF 5.0                                          page 28          TIFF 5.0                                          page 28


          Appendix B:  Data Compression_Scheme 2
          
          
          Abstract
          
          This document  describes a  method for  compressing bilevel  data
          that is  based on  the CCITT  Group 3  1D  facsimile  compression
          scheme.
          
          
          References
          
          1.   _Standardization of Group 3 facsimile apparatus for document
          transmission,_ Recommendation  T.4, Volume  VII, Fascicle  VII.3,
          Terminal Equipment  and Protocols  for  Telematic  Services,  The
          International  Telegraph  and  Telephone  Consultative  Committee
          (CCITT), Geneva, 1985, pages 16 through 31.
          2.   _Facsimile Coding  Schemes and  Coding Control Functions for
          Group 4  Facsimile Apparatus,_  Recommendation T.6,  Volume  VII,
          Fascicle VII.3,  Terminal Equipment  and Protocols  for Telematic
          Services, The  International Telegraph and Telephone Consultative
          Committee (CCITT), Geneva, 1985, pages 40 through 48.
          
          We do  not believe that these documents are necessary in order to
          implement Compression=2.   We  have included  (verbatim  in  most
          places) all the pertinent information in this Appendix.  However,
          if you  wish to  order the  documents, you  can  write  to  ANSI,
          Attention: Sales,  1430 Broadway, New York, N.Y., 10018.  Ask for
          the publication  listed above_it contains both Recommendation T.4
          and T.6.
          
          
          Relationship to the CCITT Specifications
          
          The  CCITT   Group  3   and  Group   4  specifications   describe
          communications protocols for a particular class of devices.  They
          are not  by themselves sufficient to describe a disk data format.
          Fortunately, however,  the CCITT  coding schemes  can be  readily
          adapted to this different environment.  The following is one such
          adaptation.   Most of  the language  is copied  directly from the
          CCITT specifications.
          
          
          Coding Scheme
          
          A line  (row) of  data is composed of a series of variable length
          code words.  Each code word represents a run length of either all
          white or  all black.   (Actually,  more than one code word may be
          required to  code a  given run,  in a  manner  described  below.)
          White runs and black runs alternate.
          
          In order  to ensure  that the  receiver (decompressor)  maintains
          color synchronization, all data lines will begin with a white run
          length code  word set.   If  the actual  scan line  begins with a









          TIFF 5.0                                          page 29          TIFF 5.0                                          page 29


          black run,  a white  run length  of zero  will be sent (written).
          Black or  white run  lengths are  defined by  the code  words  in
          Tables 1  and 2.   The  code words are of two types:  Terminating
          code  words   and  Make-up  code  words.    Each  run  length  is
          represented by  zero or  more  Make-up  code  words  followed  by
          exactly one Terminating code word.
          
          Run lengths  in the  range of  0 to  63 pels (pixels) are encoded
          with their appropriate Terminating code word.  Note that there is
          a different list of code words for black and white run lengths.
          
          Run lengths in the range of 64 to 2623 (2560+63) pels are encoded
          first by  the Make-up  code word representing the run length that
          is nearest  to, not  longer than,  that required.   This  is then
          followed by the Terminating code word representing the difference
          between the required run length and the run length represented by
          the Make-up code.
          
          Run lengths  in the range of lengths longer than or equal to 2624
          pels are  coded first  by the  Make-up code  of  2560.    If  the
          remaining part  of the run (after the first Make-up code of 2560)
          is 2560  pels or  greater, additional Make-up code(s) of 2560 are
          issued until the remaining part of the run becomes less than 2560
          pels.   Then  the  remaining  part  of  the  run  is  encoded  by
          Terminating code  or  by  Make-up  code  plus  Terminating  code,
          according to the range mentioned above.
          
          It is  considered an  unrecoverable error  if the  sum of the run
          lengths for  a line  does not  equal the  value of the ImageWidth
          field.
          
          New rows always begin on the next available byte boundary.
          
          No EOL  code words  are used.   No fill bits are used, except for
          the ignored  bits at  the end  of the last byte of a row.  RTC is
          not used.
          
          
          Table 1/T.4  Terminating codes
          
          
          White          Black
           run Code  run Code
          length    word length    word
           ----     ---- ------    ----
          
           0   00110101   0   0000110111
           1   000111     1   010
           2   0111  2   11
           3   1000  3   10
           4   1011  4   011
           5   1100  5   0011
           6   1110  6   0010
           7   1111  7   00011









          TIFF 5.0                                          page 30          TIFF 5.0                                          page 30


           8   10011      8   000101
           9   10100      9   000100
          10   00111     10   0000100
          11   01000     11   0000101
          12   001000    12   0000111
          13   000011    13   00000100
          14   110100    14   00000111
          15   110101    15   000011000
          16   101010    16   0000010111
          17   101011    17   0000011000
          18   0100111   18   0000001000
          19   0001100   19   00001100111
          20   0001000   20   00001101000
          21   0010111   21   00001101100
          22   0000011   22   00000110111
          23   0000100   23   00000101000
          24   0101000   24   00000010111
          25   0101011   25   00000011000
          26   0010011   26   000011001010
          27   0100100   27   000011001011
          28   0011000   28   000011001100
          29   00000010  29   000011001101
          30   00000011  30   000001101000
          31   00011010  31   000001101001
          32   00011011  32   000001101010
          33   00010010  33   000001101011
          34   00010011  34   000011010010
          35   00010100  35   000011010011
          36   00010101  36   000011010100
          37   00010110  37   000011010101
          38   00010111  38   000011010110
          39   00101000  39   000011010111
          40   00101001  40   000001101100
          41   00101010  41   000001101101
          42   00101011  42   000011011010
          43   00101100  43   000011011011
          44   00101101  44   000001010100
          45   00000100  45   000001010101
          46   00000101  46   000001010110
          47   00001010  47   000001010111
          48   00001011  48   000001100100
          49   01010010  49   000001100101
          50   01010011  50   000001010010
          51   01010100  51   000001010011
          52   01010101  52   000000100100
          53   00100100  53   000000110111
          54   00100101  54   000000111000
          55   01011000  55   000000100111
          56   01011001  56   000000101000
          57   01011010  57   000001011000
          58   01011011  58   000001011001
          59   01001010  59   000000101011
          60   01001011  60   000000101100
          61   00110010  61   000001011010









          TIFF 5.0                                          page 31          TIFF 5.0                                          page 31


          62   00110011  62   000001100110
          63   00110100  63   000001100111   
          
          
          
          
          Table 2/T.4  Make-up codes
          
          White          Black
           run Code  run Code
          length    word      length    word
          ------    ---- ------    ----
          
            64 11011       64 0000001111
           128 10010      128 000011001000
           192 010111     192 000011001001
           256 0110111    256 000001011011
           320 00110110   320 000000110011
           384 00110111   384 000000110100
           448 01100100   448 000000110101
           512 01100101   512 0000001101100
           576 01101000   576 0000001101101
           640 01100111   640 0000001001010
           704 011001100  704 0000001001011
           768 011001101  768 0000001001100
           832 011010010  832 0000001001101
           896 011010011  896 0000001110010
           960 011010100  960 0000001110011
          1024 011010101 1024 0000001110100
          1088 011010110 1088 0000001110101
          1152 011010111 1152 0000001110110
          1216 011011000 1216 0000001110111
          1280 011011001 1280 0000001010010
          1344 011011010 1344 0000001010011
          1408 011011011 1408 0000001010100
          1472 010011000 1472 0000001010101
          1536 010011001 1536 0000001011010
          1600 010011010 1600 0000001011011
          1664 011000    1664 0000001100100
          1728 010011011 1728 0000001100101
           EOL 000000000001    EOL 000000000001
          
          
          
          
          Additional make-up codes
          
          White
          and
          Black     Make-up
          run  code
          length    word
          ------    ----
          









          TIFF 5.0                                          page 32          TIFF 5.0                                          page 32


          1792 00000001000
          1856 00000001100
          1920 00000001101
          1984 000000010010
          2048 000000010011
          2112 000000010100
          2176 000000010101
          2240 000000010110
          2304 000000010111
          2368 000000011100
          2432 000000011101
          2496 000000011110
          2560 000000011111
          
          
          
          














































          TIFF 5.0                                          page 33          TIFF 5.0                                          page 33


          Appendix C: Data Compression_Scheme 32773_
          _PackBits_
          
          
          Abstract
          
          This document  describes a  simple compression scheme for bilevel
          scanned and paint type files.
          
          
          Motivation
          
          The TIFF  specification defines  a number of compression schemes.
          Compression type  1 is  really no  compression, other  than basic
          pixel  packing.     Compression   type  2,   based  on  CCITT  1D
          compression,  is   powerful,  but   not  trivial   to  implement.
          Compression type  5 is  typically very effective for most bilevel
          images, as  well as  many deeper images such as palette color and
          grayscale images, but is also not trivial to implement.  PackBits
          is a simple but often effective alternative.
          
          
          Description
          
          Several good schemes were already in use in various settings.  We
          somewhat arbitrarily picked the Macintosh PackBits scheme.  It is
          byte oriented,  so there  is no problem with word alignment.  And
          it has a good worst case behavior (at most 1 extra byte for every
          128 input  bytes).    For  Macintosh  users,  there  are  toolbox
          utilities PackBits  and UnPackBits that will do the work for you,
          but it is easy to implement your own routines.
          
          A pseudo code fragment to unpack might look like this:
          
          Loop  until  you  get  the  number  of  unpacked  bytes  you  are
          expecting:
               Read the next source byte into n.
               If n is between 0 and 127 inclusive, copy the next n+1 bytes
          literally.
               Else if  n is  between -127  and -1 inclusive, copy the next
          byte -n+1 times.
               Else if n is 128, noop.
          Endloop
          
          In the  inverse routine,  it_s best to encode a 2-byte repeat run
          as a replicate run except when preceded and followed by a literal
          run, in  which case it_s best to merge the three into one literal
          run.  Always encode 3-byte repeats as replicate runs.
          
          So that_s the algorithm.  Here are some other rules:
          
          Ñ    Each row  must be packed separately.  Do not compress across
          row boundaries.










          TIFF 5.0                                          page 34          TIFF 5.0                                          page 34


          Ñ    The number  of uncompressed  bytes per  row is defined to be
          (ImageWidth +  7) / 8.  If the uncompressed bitmap is required to
          have an  even number  of bytes  per row,  decompress  into  word-
          aligned buffers.
          Ñ    If a  run is  larger  than  128  bytes,  simply  encode  the
          remainder of the run as one or more additional replicate runs.
          
          When  PackBits   data  is  uncompressed,  the  result  should  be
          interpreted as per compression type 1 (no compression).
          





















































          TIFF 5.0                                          page 35          TIFF 5.0                                          page 35


          Appendix D
          
          
          Appendix D  has been  deleted.   It formerly contained guidelines
          for passing  TIFF files on the Microsoft Windows Clipboard.  This
          was judged to not be a good idea, in light of the ever-increasing
          size of  scanned images.   Applications are instead encouraged to
          employ file-based  mechanisms to  exchange  TIFF  data.    Aldus_
          PageMaker, for  example, implements  a _File  Place_  command  to
          allow TIFF files to be imported.
          




















































          TIFF 5.0                                          page 36          TIFF 5.0                                          page 36


          Appendix E:  Numerical List of TIFF Tags
          
          
          NewSubfileType
          Tag  =  254  (FE)
          Type = LONG
          N    = 1
          
          SubfileType
          Tag  = 255  (FF)
          Type = SHORT
          N    = 1
          
          ImageWidth
          Tag  = 256  (100)
          Type = SHORT or LONG
          N    = 1
          
          ImageLength
          Tag  = 257  (101)
          Type = SHORT or LONG
          N    = 1
          
          BitsPerSample
          Tag  = 258  (102)
          Type = SHORT
          N    = SamplesPerPixel
          
          Compression
          Tag  = 259  (103)
          Type = SHORT
          N    = 1
          
          PhotometricInterpretation
          Tag  = 262  (106)
          Type = SHORT
          N    = 1
          
          
          Threshholding
          Tag  = 263  (107)
          Type = SHORT
          N    = 1
          
          CellWidth
          Tag  = 264  (108)
          Type = SHORT
          N    = 1
          
          CellLength
          Tag  = 265  (109)
          Type = SHORT
          N    = 1
          









          TIFF 5.0                                          page 37          TIFF 5.0                                          page 37


          FillOrder
          Tag  = 266  (10A)
          Type = SHORT
          N    = 1
          
          DocumentName
          Tag  = 269  (10D)
          Type = ASCII
          
          ImageDescription
          Tag  = 270 (10E)
          Type = ASCII
          
          Make
          Tag  = 271  (10F)
          Type = ASCII
          
          Model
          Tag  = 272  (110)
          Type = ASCII
          
          StripOffsets
          Tag  = 273  (111)
          Type = SHORT or LONG
          N    = StripsPerImage for PlanarConfiguration equal to 1.
               = SamplesPerPixel  * StripsPerImage  for PlanarConfiguration
          equal to 2
          
          Orientation
          Tag  = 274 (112)
          Type = SHORT
          N    = 1
          
          SamplesPerPixel
          Tag  = 277  (115)
          Type = SHORT
          N    = 1
          
          RowsPerStrip
          Tag  = 278  (116)
          Type = SHORT or LONG
          N    = 1
          
          StripByteCounts
          Tag  = 279  (117)
          Type = LONG or SHORT
          N    = StripsPerImage for PlanarConfiguration equal to 1.
               = SamplesPerPixel  * StripsPerImage  for PlanarConfiguration
          equal to 2.
          
          MinSampleValue
          Tag  = 280  (118)
          Type = SHORT
          N    = SamplesPerPixel









          TIFF 5.0                                          page 38          TIFF 5.0                                          page 38


          
          MaxSampleValue
          Tag  = 281  (119)
          Type = SHORT
          N    = SamplesPerPixel
          
          XResolution
          Tag  = 282  (11A)
          Type = RATIONAL
          N    = 1
          
          YResolution
          Tag  = 283  (11B)
          Type = RATIONAL
          N    = 1
          
          PlanarConfiguration
          Tag  = 284  (11C)
          Type = SHORT
          N    = 1
          
          PageName
          Tag  = 285  (11D)
          Type = ASCII
          
          
          XPosition
          Tag  = 286  (11E)
          Type = RATIONAL
          
          YPosition
          Tag  = 287  (11F)
          Type = RATIONAL
          
          FreeOffsets
          Tag  = 288  (120)
          Type = LONG
          
          FreeByteCounts
          Tag  = 289  (121)
          Type = LONG
          
          GrayResponseUnit
          Tag  = 290 (122)
          Type = SHORT
          N    = 1
          
          GrayResponseCurve
          Tag  = 291 (123)
          Type = SHORT
          N    = 2**BitsPerSample
          
          Group3Options
          Tag  = 292  (124)









          TIFF 5.0                                          page 39          TIFF 5.0                                          page 39


          Type = LONG
          N    = 1
          
          Group4Options
          Tag  =  293  (125)
          Type = LONG
          N    = 1
          
          ResolutionUnit
          Tag  = 296 (128)
          Type = SHORT
          N    = 1
          
          PageNumber
          Tag  = 297  (129)
          Type = SHORT
          N    = 2
          
          ColorResponseCurves
          Tag  = 301 (12D)
          Type = SHORT
          N    = 3 * (2**BitsPerSample)
          
          Software
          Tag  = 305  (131)
          Type = ASCII
          
          DateTime
          Tag  = 306  (132)
          Type = ASCII
          N    = 20
          
          Artist
          Tag  = 315  (13B)
          Type = ASCII
          
          HostComputer
          Tag  = 316  (13C)
          Type = ASCII
          
          Predictor
          Tag  = 317 (13D)
          Type = SHORT
          N    = 1
          
          WhitePoint
          Tag  = 318 (13E)
          Type = RATIONAL
          N    = 2
          
          PrimaryChromaticities
          Tag  = 319 (13F)
          Type = RATIONAL
          N    = 6









          TIFF 5.0                                          page 40          TIFF 5.0                                          page 40


          
          ColorMap
          Tag  = 320 (140)
          Type = SHORT
          N    = 3 * (2**BitsPerSample)
          

























































          TIFF 5.0                                          page 41          TIFF 5.0                                          page 41


          Appendix F:  Data Compression_Scheme 5_LZW
          Compression
          
          
          Abstract
          
          This document describes an adaptive compression scheme for raster
          images.
          
          
          Reference
          
          Terry  A.   Welch,  _A   Technique  for   High  Performance  Data
          Compression_,  IEEE   Computer,  vol.   17  no.  6  (June  1984).
          Describes the  basic Lempel-Ziv  & Welch  (LZW) algorithm.    The
          author_s goal  in the  article is  to describe  a  hardware-based
          compressor that could be built into a disk controller or database
          engine, and  used on  all types  of data.   There  is no specific
          discussion of  raster images.    We  intend  to  give  sufficient
          information in  this Appendix so that the article is not required
          reading.
          
          
          Requirements
          
          A compression  scheme with  the following  characteristics should
          work well in a desktop publishing environment:
          
          Ñ    Must work well for images of any bit depth, including images
          deeper than 8 bits per sample.
          Ñ    Must be effective:  an average compression ratio of at least
          2:1 or  better.    And  it  must  have  a  reasonable  worst-case
          behavior, in case something really strange is thrown at it.
          Ñ    Should  not  depend  on  small  variations  between  pixels.
          Palette color  images tend  to contain  abrupt changes  in  index
          values, due to common patterning and dithering techniques.  These
          abrupt changes  do tend to be repetitive, however, and the scheme
          should make use of this fact.
          Ñ    For images  generated by  paint programs,  the scheme should
          not depend on a particular pattern width.  8x8 pixel patterns are
          common now, but we should not assume that this situation will not
          change.
          Ñ    Must be  fast.   It should  not take  more than 5 seconds to
          decompress a  100K byte  grayscale image on a 68020- or 386-based
          computer.   Compression can  be slower,  but probably not by more
          than a factor of 2 or 3.
          Ñ    The level  of implementation  complexity must be reasonable.
          We would like something that can be implemented in no more than a
          couple of  weeks  by  a_competent  software  engineer  with  some
          experience  in   image  processing.     The   compiled  code  for
          compression and  decompression combined  should be  no more  than
          about 10K.
          Ñ    Does not require floating point software or hardware.
          









          TIFF 5.0                                          page 42          TIFF 5.0                                          page 42


          
          The following  sections describe  an algorithm based on the _LZW_
          (Lempel-Ziv & Welch) technique that meets the above requirements.
          In addition  meeting our  requirements,  LZW  has  the  following
          characteristics:
          
          Ñ    LZW is fully reversible.  All information is preserved.  But
          if noise  or information  is removed  from an  image, perhaps  by
          smoothing or  zeroing some  low-order bitplanes,  LZW  compresses
          images to  a smaller  size.   Thus,   5-bit, 6-bit, or 7-bit data
          masquerading as  8-bit data  compresses better  than  true  8-bit
          data. Smooth  images also  compress better than noisy images, and
          simple images compress better than complex images.
          í    On a  68082- or  386-based computer,  LZW  software  can  be
          written to  compress at  between 30K  and 80K  bytes per  second,
          depending on image characteristics.  LZW decompression speeds are
          typically about 50K bytes per second.
          í    LZW works  well on  bilevel images,  too.   It always  beats
          PackBits,  and   generally  ties   CCITT  1D  (Modified  Huffman)
          compression, on our test images.  Tying CCITT 1D is impressive in
          that LZW  seems to be considerably faster than CCITT 1D, at least
          in our implementation.
          í    Our implementation is written in C, and compiles to about 2K
          bytes of object code each for the compressor and decompressor.
          í    One of  the nice  things about  LZW is that it is used quite
          widely in  other applications  such as  archival programs, and is
          therefore more of a known quantity.
          
          
          The Algorithm
          
          Each strip  is compressed  independently.   We strongly recommend
          that RowsPerStrip  be chosen  such that each strip contains about
          8K bytes  before compression.   We  want to keep the strips small
          enough so  that the  compressed and  uncompressed versions of the
          strip can  be kept entirely in memory even on small machines, but
          large enough to maintain nearly optimal compression ratios.
          
          The LZW  algorithm is  based on  a translation  table, or  string
          table, that  maps strings  of input  characters into  codes.  The
          TIFF implementation  uses variable-length  codes, with  a maximum
          code length of 12 bits.  This string table is different for every
          strip, and,  remarkably, does  not need to be kept around for the
          decompressor.     The  trick   is  to   make   the   decompressor
          automatically build  the same  table as is built when compressing
          the data.   We  use a  C-like pseudocode  to describe  the coding
          scheme:
          
               InitializeStringTable();
               WriteCode(ClearCode);
               _ = the empty string;
               for each character in the strip {
                    K = GetNextCharacter();
                    if _+K is in the string table {









          TIFF 5.0                                          page 43          TIFF 5.0                                          page 43


                         _ = _+K;  /* string concatenation */
                    } else {
                         WriteCode (CodeFromString(_));
                         AddTableEntry(_+K);
                         _ = K;
                    }
               } /* end of for loop */
               WriteCode (CodeFromString(_));
               WriteCode (EndOfInformation);
                    
          That_s  it.    The  scheme  is  simple,  although  it  is  fairly
          challenging  to  implement  efficiently.    But  we  need  a  few
          explanations before we go on to decompression.
          
          The  _characters_   that  make  up  the  LZW  strings  are  bytes
          containing TIFF  uncompressed (Compression=1)  image data, in our
          implementation.   For example,  if BitsPerSample is 4, each 8-bit
          LZW character will contain two 4-bit pixels.  If BitsPerSample is
          16, each 16-bit pixel will span two 8-bit LZW characters.
          
          (It is  also possible to implement a version of LZW where the LZW
          character depth equals BitsPerSample, as was described by Draft 2
          of Revision  5.0.   But  there  is  a  major  problem  with  this
          approach.   If BitsPerSample  is greater  than 11, we can not use
          12-bit-maximum  codes,   so  that  the  resulting  LZW  table  is
          unacceptably large.   Fortunately,  due to the adaptive nature of
          LZW, we  do not  pay a  significant compression ratio penalty for
          combining several  pixels into  one byte before compressing.  For
          example, our  4-bit sample  images  compressed  about  3  percent
          worse, and  our 1-bit  images compressed  about 5 percent better.
          And it  is easier to write an LZW compressor that always uses the
          same character  depth than  it is  to write  one which can handle
          varying depths.)
          
          We can  now describe  some of the routine and variable references
          in our pseudocode:
          
          InitializeStringTable() initializes  the string  table to contain
          all possible  single-character strings.   There  are 256 of them,
          numbered 0 through 255, since our characters are bytes.
          
          WriteCode() writes  a code  to the output stream.  The first code
          written is a Clear code, which is defined to be code #256.
          
          _ is our _prefix string._
          
          GetNextCharacter() retrieves  the next  character value  from the
          input stream.   This  will be number between 0 and 255, since our
          characters are bytes.
          
          The _+_ signs indicate string concatenation.
          
          AddTableEntry() adds a table entry.  (InitializeStringTable() has
          already put  256 entries  in our table.  Each entry consists of a









          TIFF 5.0                                          page 44          TIFF 5.0                                          page 44


          single-character string, and its associated code value, which is,
          in our  application, identical to the character itself.  That is,
          the 0th  entry in  our table  consists of  the string  <0>,  with
          corresponding code  value of  <0>, the  1st entry  in  the  table
          consists of the string <1>, with corresponding code value of <1>,
          ..., and  the 255th  entry in  our table  consists of  the string
          <255>, with  corresponding code  value of  <255>.)   So the first
          entry that  we add  to our  string table will be at position 256,
          right?   Well, not  quite, since  we will reserve code #256 for a
          special   _Clear_   code,   and   code   #257   for   a   special
          _EndOfInformation_ code  that we will write out at the end of the
          strip.  So the first multiple-character entry added to the string
          table will be at position 258.
          
          Let_s try  an example.   Suppose  we have  input data  that looks
          like:
          
          Pixel 0:  <7>
          Pixel 1:  <7>
          Pixel 2:  <7>
          Pixel 3:  <8>
          Pixel 4:  <8>
          Pixel 5:  <7>
          Pixel 6:  <7>
          Pixel 7:  <6>
          Pixel 8:  <6>
          
          First, we read Pixel 0 into K.  _K is then simply <7>, since _ is
          the empty string at this point.  Is the string <7> already in the
          string table?  Of course, since all single character strings were
          put in  the table  by InitializeStringTable().  So set _ equal to
          <7>, and go to the top of the loop.
          
          Read Pixel 1 into K.  Does _K (<7><7>) exist in the string table?
          No, so we get to do some real work.  We write the code associated
          with _  to output  (write <7>  to output), and add _K (<7><7>) to
          the table  as entry  258.   Store K  (<7>) into  _.    Note  that
          although we have added the string consisting of Pixel 0 and Pixel
          1 to  the table, we _re-use_ Pixel 1 as the beginning of the next
          string.
          
          Back at  the top  of the  loop.  We read Pixel 2 into K.  Does _K
          (<7><7>) exist  in the  string table?   Yes,  the entry  we  just
          added, entry 258, contains exactly <7><7>.  So we just add K onto
          the end of _, so that _ is now <7><7>.
          
          Back at  the top  of the  loop.  We read Pixel 3 into K.  Does _K
          (<7><7><8>) exist  in the  string table?   No,  so write the code
          associated with  _ (<258>)  to output, and add _K to the table as
          entry 259.  Store K (<8>) into _.
          
          Back at  the top  of the  loop.  We read Pixel 4 into K.  Does _K
          (<8><8>) exist  in the  string table?   No,  so  write  the  code










          TIFF 5.0                                          page 45          TIFF 5.0                                          page 45


          associated with  _ (<8>)  to output,  and add  _K to the table as
          entry 260.  Store K (<8>) into _.
          
          Continuing, we get the following results:
          
               After reading: We write to output: And add table entry:
               Pixel 0
               Pixel 1   <7>  258: <7><7>
               Pixel 2
               Pixel 3   <258>     259: <7><7><8>
               Pixel 4   <8>  260: <8><8>
               Pixel 5   <8>  261: <8><7>
               Pixel 6
               Pixel 7   <258>     262: <7><7><6>
               Pixel 8   <6>  263: <6><6>
          
          WriteCode() also  requires some  explanation.   The  output  code
          stream,  <7><258><8><8><258><6>...  in  our  example,  should  be
          written using as few bits as possible.  When we are just starting
          out, we  can use  9-bit codes, since our new string table entries
          are greater  than 255  but less  than 512.  But when we add table
          entry 512,  we must  switch to 10-bit codes.  Likewise, we switch
          to 11-bit  codes at  1024, and  12-bit codes  at 2048.   We  will
          somewhat arbitrarily limit ourselves to 12-bit codes, so that our
          table can  have at most 4096 entries.  If we push it any farther,
          tables tend to get too large.
          
          What happens  if we run out of room in our string table?  This is
          where the afore-mentioned Clear code comes in.  As soon as we use
          entry 4094, we write out a (12-bit) Clear code.   (If we wait any
          longer to  write the  Clear code,  the decompressor  might try to
          interpret the  Clear code  as a 13-bit code.)  At this point, the
          compressor re-initializes the string table and starts writing out
          9-bit codes again.
          
          Note that  whenever you  write a code and add a table entry, _ is
          not left  empty.   It contains exactly one character.  Be careful
          not to  lose it  when you  write an end-of-table Clear code.  You
          can either write it out as a 12-bit code before writing the Clear
          code, in  which case  you will  want to  do it right after adding
          table entry  4093, or  after the  clear code  as  a  9-bit  code.
          Decompression gives the same result in either case.
          
          To make  things a  little simpler  for the  decompressor, we will
          require that  each strip  begins with a Clear code, and ends with
          an EndOfInformation code.
          
          Every LZW-compressed  strip must  begin on  a byte  boundary.  It
          need not  begin on  a word  boundary.   LZW compression codes are
          stored into  bytes in  high-to-low-order fashion, i.e., FillOrder
          is assumed  to be  1.  The compressed codes are written as bytes,
          not  words,  so  that  the  compressed  data  will  be  identical
          regardless of whether it is an _II_ or _MM_ file.
          









          TIFF 5.0                                          page 46          TIFF 5.0                                          page 46


          Note that  the LZW string table is a continuously updated history
          of the  strings that  have been encountered in the data.  It thus
          reflects the characteristics of the data, providing a high degree
          of adaptability.
          
          
          LZW Decoding
          
          The procedure for decompression is a little more complicated, but
          still not too bad:
                    
               while ((Code = GetNextCode()) != EoiCode) {
                    if (Code == ClearCode) {
                         InitializeTable();
                         Code = GetNextCode();
                         if (Code == EoiCode)
                              break;
                         WriteString(StringFromCode(Code));
                         OldCode = Code;
                    }  /* end of ClearCode case */
          
                    else {
                         if (IsInTable(Code)) {
                              WriteString(StringFromCode(Code));
                              AddStringToTable(StringFromCode(OldCode)+Firs
          tChar(StringFromCode(Code)));
                              OldCode = Code;
                         } else {
                              OutString   =    StringFromCode(OldCode)    +
          FirstChar(StringFromCode(OldCode));
                              WriteString(OutString);
                              AddStringToTable(OutString);
                              OldCode = Code;
                         }
                    } /* end of not-ClearCode case */
               } /* end of while loop */
          
          The function  GetNextCode() retrieves the next code from the LZW-
          coded data.  It must keep track of bit boundaries.  It knows that
          the first code that it gets will be a 9-bit code.  We add a table
          entry each  time we get a code, so GetNextCode() must switch over
          to 10-bit codes as soon as string #511 is stored into the table.
          
          The function  StringFromCode() gets  the string associated with a
          particular code from the string table.
          
          The function  AddStringToTable() adds  a  string  to  the  string
          table.   The _+_  sign joining  the two  parts of the argument to
          AddStringToTable indicate string concatenation.
          
          StringFromCode() looks  up the  string associated  with  a  given
          code.
          
          WriteString() adds a string to the output stream.









          TIFF 5.0                                          page 47          TIFF 5.0                                          page 47


          
          
          When SamplesPerPixel Is Greater Than 1
          
          We  have   so  far   described  the   compression  scheme  as  if
          SamplesPerPixel were  always 1,  as will  be  be  the  case  with
          palette color  and grayscale  images.  But what do we do with RGB
          image data?
          
          Tests on  our sample  images indicate  that the  LZW  compression
          ratio    is    nearly    identical    regardless    of    whether
          PlanarConfiguration=1 or  PlanarConfiguration=2, for  RGB images.
          So use  whichever configuration  you prefer,  and simply compress
          the bytes in the strip.
          
          It is  worth cautioning  that compression  ratios on our test RGB
          images were disappointing low: somewhere between 1.1 to 1 and 1.5
          to 1,  depending on the image.  Vendors are urged to do what they
          can to  remove as  much noise  from  their  images  as  possible.
          Preliminary tests  indicate that significantly better compression
          ratios are  possible with  less noisy  images.  Even something as
          simple as  zeroing out one or two least-significant bitplanes may
          be  quite   effective,  with   little  or  no  perceptible  image
          degradation.
          
          
          Implementation
          
          The exact  structure of  the string  table and the method used to
          determine if  a string  is already  in the table are probably the
          most significant  design decisions in the implementation of a LZW
          compressor and  decompressor.   Hashing has  been suggested  as a
          useful technique for the compressor.  We have chosen a tree based
          approach, with  good results.   The decompressor is actually more
          straightforward,  as   well  as   faster,  since   no  search  is
          involved_strings can be accessed directly by code value.
          
          
          Performance
          
          Many  people   do  not   realize  that  the  performance  of  any
          compression scheme  depends greatly  on the type of data to which
          it is  applied.   A scheme that works well on one data set may do
          poorly on the next.
          
          But since  we do  not want  to burden  the world  with  too  many
          compression schemes, an adaptive scheme such as LZW that performs
          quite well  on a wide range of images is very desirable.  LZW may
          not always  give optimal  compression ratios,  but  its  adaptive
          nature and relative simplicity seem to make it a good choice.
          
          Experiments thus  far indicate  that we  can  expect  compression
          ratios of  between 1.5  and 3.0  to 1  from LZW,  with no loss of
          data, on  continuous tone  grayscale scanned  images.  If we zero









          TIFF 5.0                                          page 48          TIFF 5.0                                          page 48


          the least  significant one or two bitplanes of 8-bit data, higher
          ratios can be achieved.  These bitplanes often consist chiefly of
          noise, in  which case  little or no loss in image quality will be
          perceived.   Palette color  images created  in  a  paint  program
          generally compress  much  better  than  continuous  tone  scanned
          images, since paint images tend to be more repetitive.  It is not
          unusual to  achieve compression  ratios of 10 to 1 or better when
          using LZW on palette color paint images.
          
          By way  of comparison, PackBits, used in TIFF for black and white
          bilevel images, does not do well on color paint images, much less
          continuous tone  grayscale and  color images.  1.2 to 1 seemed to
          be about average for 4-bit images, and 8-bit images are worse.
          
          It has  been suggested that the CCITT 1D scheme could be used for
          continuous tone  images, by compressing each bitplane separately.
          No doubt  some  compression  could  be  achieved,  but  it  seems
          unlikely that  a scheme  based on a fixed table that is optimized
          for short  black runs  separated by  longer white runs would be a
          very good choice on any of the bitplanes.  It would do quite well
          on the  high-order bitplanes  (but so would a simpler scheme like
          PackBits), and  would do quite poorly on the low-order bitplanes.
          We believe  that the  compression ratios  would generally  not be
          very impressive, and the process would in addition be quite slow.
          Splitting  the  pixels  into  bitplanes  and  putting  them  back
          together is  somewhat expensive,  and the  coding is  also fairly
          slow when implemented in software.
          
          Another  approach   that  has  been  suggested  uses  uses  a  2D
          differencing step  following by  coding the  differences using  a
          fixed table  of variable-length codes.  This type of scheme works
          quite well  on many  8-bit  grayscale  images,  and  is  probably
          simpler  to  implement  than  LZW.    But  it  has  a  number  of
          disadvantages when  used on  a wide variety of images.  First, it
          is not  adaptive.   This makes  a big difference when compressing
          data such as 8-bit images that have been _sharpened_ using one of
          the standard  techniques.  Such images tend to get larger instead
          of smaller  when  compressed.    Another  disadvantage  of  these
          schemes is  that they  do not  do well  with a  wide range of bit
          depths.   The built-in  code table  has to  be  optimized  for  a
          particular bit depth in order to be effective.
          
          Finally,  we   should  mention   _lossy_   compression   schemes.
          Extensive research  has been  done in  the area of lossy, or non-
          information-preserving  image   compression.    These  techniques
          generally yield  much  higher  compression  ratios  than  can  be
          achieved  by   fully-reversible,   information-preserving   image
          compression  techniques   such  as   PackBits  and   LZW.    Some
          disadvantages:     many  of   the   lossy   techniques   are   so
          computationally expensive  that hardware  assists  are  required.
          Others  are  so  complicated  that  most  microcomputer  software
          vendors could  not afford either the expense of implementation or
          the increase  in  application  object  code  size.    Yet  others










          TIFF 5.0                                          page 49          TIFF 5.0                                          page 49


          sacrifice enough  image  quality  to  make  them  unsuitable  for
          publishing use.
          
          In spite  of these  difficulties, we  believe that there will one
          day be  a standardized  lossy compression  scheme for  full color
          images  that  will  be  usable  for  publishing  applications  on
          microcomputers.   An International  Standards Organization group,
          ISO/IEC/JTC1/SC2/WG8, in cooperation with CCITT Study Group VIII,
          is hard at work on a scheme that might be appropriate.  We expect
          that a  future revision of TIFF will incorporate this scheme once
          it is  finalized, if it turns out to satisfy the needs of desktop
          publishers and  others in the microcomputer community.  This will
          augment, not replace, LZW as an approved TIFF compression scheme.
          LZW will  very likely  remain the  scheme of  choice for  Palette
          color images,  and perhaps  4-bit grayscale  images, and may well
          overtake CCITT 1D and PackBits for bilevel images.
          
          
          Future LZW Extensions
          
          Some images  compress better  using LZW  coding if they are first
          subjected to  a process  wherein each  pixel value is replaced by
          the  difference  between  the  pixel  and  the  preceding  pixel.
          Performing this  differencing in two dimensions helps some images
          even more.  However, many images do not compress better with this
          extra preprocessing,  and for a significant number of images, the
          compression ratio is actually worse.  We are therefore not making
          differencing an integral part of the TIFF LZW compression scheme.
          
          However,  it   is  possible   that  a   _prediction_  stage  like
          differencing may  exist which  is effective over a broad range of
          images.  If such a scheme is found, it may be incorporated in the
          next major TIFF revision.  If so, a new value will be defined for
          the new  _Predictor_ TIFF  tag.  Therefore, all TIFF readers that
          read LZW files must pay attention to the Predictor tag.  If it is
          1, which  is the  default case,  LZW  decompression  may  proceed
          safely.   If it  is not  1, and the reader does not recognize the
          specified prediction scheme, the reader should give up.
          
          
          Acknowledgements
          
          The original  LZW reference  has already  been given.  The use of
          ClearCode as a technique to handle overflow was borrowed from the
          compression scheme used by the Graphics Interchange Format (GIF),
          a small-color-paint-image-file  format used  by  CompuServe  that
          also is an adaptation of the LZW technique.  Joff Morgan and Eric
          Robinson of  Aldus were  each instrumental  in their  own way  in
          getting LZW off the ground.
          













          TIFF 5.0                                          page 50          TIFF 5.0                                          page 50


          Appendix G: TIFF Classes
          
          
          Rationale
          
          TIFF was  designed to  make  life  easier  for  scanner  vendors,
          desktop publishing  software developers,  and users  of these two
          classes of products, by reducing the proliferation of proprietary
          scanned  image   formats.    It  has  succeeded  far  beyond  our
          expectations in  this respect.   But  we had  expected that  TIFF
          would be of interest to only a dozen or so scanner vendors (there
          weren_t any  more than  that in  1985), and  another dozen  or so
          desktop publishing  software vendors.   This  turned out  to be a
          gross underestimate.   The only problem with this sort of success
          is that  TIFF was  designed to  be powerful  and flexible, at the
          expense of  simplicity.   It takes  a fair  amount of  effort  to
          handle all  the options  currently defined  in this specification
          (probably no  application does  a  complete  job),  and  that  is
          currently the  only way  you can be sure that you will be able to
          import any  TIFF image,  since there are so many image-generating
          applications out there now.
          
          So here  is an attempt to channel some of the flexibility of TIFF
          into more  restrictive paths,  using what  we have learned in the
          past two  years about which options are the most useful.  Such an
          undertaking is  of course filled with fairly arbitrary decisions.
          But the  result is  that writers can more easily write files that
          will be  successfully read by a wide variety of applications, and
          readers can know when they can stop adding TIFF features.
          
          The price  we pay for TIFF Classes is some loss in the ability to
          adapt.   Once we  establish the requirements for a TIFF Class, we
          can never add new requirements, since old software would not know
          about these  new requirements.  (The best we can do at that point
          is establish new TIFF Classes.  But the problem with that is that
          we could quickly have too many TIFF Classes.)  So we must believe
          that we know what we are doing in establishing these Classes.  If
          we do not, any mistakes will be expensive.
          
          
          Overview
          
          Four TIFF Classes have been defined:
          
          Ñ    Class B for bilevel (1-bit) images
          Ñ    Class G for grayscale images
          Ñ    Class P for palette color images
          Ñ    Class R for RGB full color images
          
          To save  time and  space, we will usually say _TIFF B_, _TIFF G_,
          _TIFF P,_  and _TIFF R._  If we are talking about all four types,
          we may write _TIFF X._
          










          TIFF 5.0                                          page 51          TIFF 5.0                                          page 51


          (Note to  fax people:   if  you are  interested in  a fax  TIFF F
          Class, please  get together  and decide  what should  be in  TIFF
          Class F  files.  Let us know if we can help in any way.  When you
          have decided,  send us  your results,  so that we can include the
          information here.)
          
          
          Core Requirements
          
          This section  describes requirements  that are common to all TIFF
          Class X images.
          
          General Requirements
          
          The following  are required  characteristics of  all TIFF Class X
          files.
          
          Where there are options, TIFF X writers can do whichever one they
          want, though  we will  often recommend  a particular  choice, but
          TIFF X  readers must  be able  to handle all of them.  Please pay
          close attention  to the  recommendations.  It is possible that at
          some point  in the future, new and even-simpler TIFF classes will
          be defined that include only recommended features.
          
          You will  need to  read at  least the first three sections of the
          main specification  in order  to fully  understand the  following
          discussion.
          
          Defaults.  TIFF X writers may, but are not required, to write out
          a field that has a default value, if the default value is the one
          desired.   TIFF X  readers must  be  prepared  to  handle  either
          situation.
          
          Other fields.   TIFF  X readers  must be  prepared  to  encounter
          fields other  than the  required fields  in TIFF X files.  TIFF X
          writers  are  allowed  to  write  fields  such  as  Make,  Model,
          DateTime, and so on, and TIFF X readers can certainly make use of
          such fields  if they  exist.   TIFF X  readers must not, however,
          refuse to read the file if such optional fields do not exist.
          
          _MM_ and  ‘II’ byte order.  TIFF X readers must be able to handle
          both byte  orders.    TIFF  writers  can  do  whichever  is  most
          convenient  or   efficient.     Images  are   crossing  the   IBM
          PC/Macintosh boundary  (and others  as well)  with a surprisingly
          high frequency.   We could force writers to all use the same byte
          order, but  preliminary evidence  indicates that  this will cause
          problems  when   we  start   seeing  greater-than-8-bit   images.
          Reversing bytes  while scanning could well slow down the scanning
          process enough  to cause  the scanning  mechanism to  stop, which
          tends to create image quality problems.
          
          Multiple subfiles.   TIFF X readers must be prepared for multiple
          images (i.e.,  subfiles) per  TIFF file,  although they  are  not
          required to do anything with any image after the first one.  TIFF









          TIFF 5.0                                          page 52          TIFF 5.0                                          page 52


          X writers  must be  sure to write a long word of 0 after the last
          IFD (this is the standard way of signalling that this IFD was the
          last one) as indicated in the TIFF structure discussion.
          
          If a  TIFF X  writer writes multiple subfiles, the first one must
          be the  full resolution  image.   Subsequent subimages,  such  as
          reduced resolution  images and  transparency masks, may be in any
          order in  the TIFF  file.   If a reader wants to make use of such
          subimages, it  will have to scan the IFD’s before deciding how to
          proceed.
          
          TIFF X  Editors.   Editors, applications  that modify TIFF files,
          have a few additional requirements.
          
          TIFF editors  must be  especially careful  about subfiles.   If a
          TIFF editor  edits a full-resolution subfile, but does not update
          an accompanying  reduced-resolution subfile,  a reader  that uses
          the reduced-resolution  subfile for  screen display  will display
          the wrong  thing.   So TIFF  editors must  either  create  a  new
          reduced-resolution subfile  when  they  alter  a  full-resolution
          subfile, or  else they  must simply delete any subfiles that they
          aren_t prepared to deal with.
          
          A similar  situation arises with the fields themselves.  A TIFF X
          editor need  only worry  about the  TIFF X  required fields.   In
          particular, it  is unnecessary,  and probably  dangerous, for  an
          editor to  copy fields  that it does not understand.  It may have
          altered the  file in  a way that is incompatible with the unknown
          fields.
          
          
          Required Fields
          
          NewSubfileType.  LONG.  Recommended but not required.
          
          ImageWidth.   SHORT or  LONG.   (That is, both _SHORT_ and _LONG_
          TIFF data  types are  allowed, and  must be  handled properly  by
          readers.   TIFF writers  can use either.)  TIFF X readers are not
          required to  read arbitrarily  large files however.  Some readers
          will give  up if the entire image cannot fit in available memory.
          (In such cases the reader should inform the user of the nature of
          the problem.)   Others  will  probably  not  be  able  to  handle
          ImageWidth greater  than 65535.   Recommendation: use LONG, since
          resolutions seem to keep going up.
          
          ImageLength.  SHORT or LONG.  Recommendation: use  LONG.
          
          RowsPerStrip.  SHORT or LONG.  Readers must be able to handle any
          value between  1 and  2**32-1.   However, some readers may try to
          read an  entire strip  into memory  at one  time, so  that if the
          entire image is one strip, the application may run out of memory.
          Recommendation 1:   Set  RowsPerStrip such  that the size of each
          strip is  about 8K  bytes.   Do this  even for uncompressed data,
          since it  is easy  for a  writer and  makes  things  simpler  for









          TIFF 5.0                                          page 53          TIFF 5.0                                          page 53


          readers.  (Note:  extremely wide, high-resolution images may have
          rows larger  than 8K  bytes; in this case, RowsPerStrip should be
          1,  and   the  strip  will  just  have  to  be  larger  than  8K.
          Recommendation 2: use LONG.
          
          StripOffsets.   SHORT or  LONG.  As explained in the main part of
          the  specification,   the  number   of  StripOffsets  depends  on
          RowsPerStrip and  ImageLength.  Recommendation:  always use LONG.
          (LONG must, of course, be used if the file is more than 64K bytes
          in length.)
          
          StripByteCounts.   SHORT or  LONG.   Many existing TIFF images do
          not contain StripByteCounts, because, in a strict sense, they are
          unnecessary.   It is  possible to  write an efficient TIFF reader
          that does  not need  to know  in advance  the  exact  size  of  a
          compressed strip.   But  it does  make things  considerably  more
          complicated, so  we will require StripByteCounts in TIFF X files.
          Recommendation:   use SHORT,  since strips are not supposed to be
          very large.
          
          XResolution, YResolution.   RATIONAL.   Note  that the  X  and  Y
          resolutions may  be unequal.   A  TIFF X  reader must  be able to
          handle this  case.   TIFF X pixel-editors will typically not care
          about the  resolution,  but  applications  such  as  page  layout
          programs will.
          
          ResolutionUnit.   SHORT.   TIFF X  readers must  be  prepared  to
          handle all three values for ResolutionUnit.
          
          
          TIFF Class B - Bilevel
          
          Required (in addition to the above core requirements)
          
          The following fields and values are required for TIFF B files, in
          addition to  the fields  required for  all  TIFF  X  images  (see
          above).
          
          SamplesPerPixel =  1.   SHORT.   (Since this  is the default, the
          field need  not be  present.   The same  thing  holds  for  other
          required TIFF X fields that have defaults.)
          
          BitsPerSample = 1.  SHORT.
          
          Compression = 1, 2 (CCITT 1D), or 32773 (PackBits).  SHORT.  TIFF
          B readers  must handle all three.  Recommendation:  use PackBits.
          It  is  simple,  effective,  fast,  and  has  a  good  worst-case
          behavior.    CCITT  1D  is  definitely  more  effective  in  some
          situations, such as scanning a page of body text, but is tough to
          implement and  test, fairly  slow,  and  has  a  poor  worst-case
          behavior.   Besides, scanning a page of 12 point text is not very
          useful for  publishing applications,  unless the  image  data  is
          turned into  ASCII text  via OCR  software, which  is outside the
          scope of TIFF.









          TIFF 5.0                                          page 54          TIFF 5.0                                          page 54


          
          PhotometricInterpretation = 0 or 1.  SHORT.
          A Sample TIFF B Image
          
          Offset         Value
          (hex)     Name (mostly hex)
          
          Header:
          0000 Byte Order     4D4D
          0002 Version   002A
          0004 1st IFD pointer     00000014
          
          IFD:
          0014 Entry Count    000D
          0016 NewSubfileType 00FE 0004 00000001  00000000
          0022 ImageWidth     0100 0004 00000001  000007D0
          002E ImageLength    0101 0004 00000001  00000BB8
          003A Compression    0103 0003 00000001  8005 0000
          0046 PhotometricInterpretation     0106 0003 00000001  0001 0000
          0052 StripOffsets   0111 0004 000000BC  000000B6
          005E RowsPerStrip   0116 0004 00000001  00000010
          006A StripByteCounts     0117 0003 000000BC  000003A6
          0076 XResolution    011A 0005 00000001  00000696
          0082 YResolution    011B 0005 00000001  0000069E
          008E Software  0131 0002 0000000E  000006A6
          009A DateTime  0132 0002 00000014  000006B6
          00A6 Next IFD pointer    00000000
          
          Fields pointed to by the tags:
          00B6 StripOffsets   Offset0, Offset1, ... Offset187
          03A6 StripByteCounts     Count0, Count1, ... Count187
          0696 XResolution    0000012C 00000001
          069E YResolution    0000012C 00000001
          06A6 Software  "PageMaker 3.0"
          06B6 DateTime  "1988:02:18 13:59:59"
          
          
          Image Data:
          00000700  Compressed data for strip 10
          xxxxxxxx  Compressed data for strip 179
          xxxxxxxx  Compressed data for strip 53
          xxxxxxxx  Compressed data for strip 160
          .
          .
          .
          
          End of example
          
          Comments on the TIFF B example
          
          1.   The IFD  in our example starts at position hex 14.  It could
          have been  anywhere in  the file  as long as the position is even
          and greater  than or equal to 8, since the TIFF header is 8 bytes
          long and must be the first thing in a TIFF file.









          TIFF 5.0                                          page 55          TIFF 5.0                                          page 55


          
          2.   With 16 rows per strip, we have 188 strips in all.
          
          3.   The example  uses a  number  of  optional  fields,  such  as
          DateTime.   TIFF X  readers must safely skip over these fields if
          they do not want to use the information.  And TIFF X readers must
          not require that such fields be present.
          
          4.   Just for  fun, our example has highly fragmented image data;
          the strips  of our  image are  not even in sequential order.  The
          point is  that strip  offsets must  not be ignored.  Never assume
          that strip  N+1 follows  strip N.    Incidentally,  there  is  no
          requirement that  the image  data follows  the  IFD  information.
          Just the follow the pointers, whether they be IFD pointers, field
          pointers, or Strip Offsets.
          
          
          
          TIFF Class G - Grayscale
          
          Required (in addition to the above core requirements)
          
          SamplesPerPixel = 1.  SHORT.
          
          BitsPerSample =  4,  8.    SHORT.    There  seems  to  be  little
          justification for  working with grayscale images shallower than 4
          bits, and 5-bit , 6-bit, and 7-bit images can easily be stored as
          8-bit images, as long as you can compress the _unused_ bit planes
          without penalty.  And we can do just that with LZW (Compression =
          5.)
          
          Compression = 1 or 5 (LZW).  SHORT.  Recommendation: use 5, since
          LZW decompression is turning out to be quite fast.
          
          PhotometricInterpretation = 0 or 1.  SHORT.   Recommendation: use
          1, due  to popular  user interfaces  for adjusting brightness and
          contrast.
          
          
          
          TIFF Class P - Palette Color
          
          Required (in addition to the above core requirements)
          
          SamplesPerPixel = 1.  SHORT.  We use each pixel value as an index
          into all three color tables in ColorMap.
          
          BitsPerSample =  1,2,3,4,5,6,7, or 8.  SHORT.  1,2,3,4, and 8 are
          probably the  most common,  but as long as we are doing that, the
          rest come pretty much for free.
          
          Compression = 1 or 5.  SHORT.
          
          PhotometricInterpretation = 3 (Palette Color).  SHORT.









          TIFF 5.0                                          page 56          TIFF 5.0                                          page 56


          
          ColorMap.  SHORT.
          
          Note that  bilevel and  grayscale images  can be  represented  as
          special cases  of palette  color images.  As soon as enough major
          applications support  palette color  images, we may want to start
          getting rid  of  distinctions  between  bilevel,  grayscale,  and
          palette color images.
          
          
          TIFF Class R - RGB Full Color
          
          Required (in addition to the above Core Requirements)
          
          SamplesPerPixel = 3.  SHORT.  One sample each for Red, Green, and
          Blue.
          
          BitsPerSample =  8,8,8.   SHORT.  Shallower samples can easily be
          stored as 8-bit samples with no penalty if the data is compressed
          with LZW.  And evidence to date indicates that images deeper than
          8 bits  per sample are not worth the extra work, even in the most
          demanding publishing applications.
          
          PlanarConfiguration = 1 or 2.  SHORT.  Recommendation:  use 1.
          
          Compression = 1 or 5.  SHORT.
          
          PhotometricInterpretation = 2 (RGB).  SHORT.
          
          Recommended
          
          Recommended for  TIFF Class  R, but not required, are the new (as
          of Revision 5.0) colorimetric information tags.  See Appendix H.
          
          
          Conformance and User Interface
          
          Applications that  write valid  TIFF X files should include _TIFF
          B_ and/or  _TIFF G_  and/or _TIFF  P_ and/or  _TIFF R_  and/or in
          their product  spec sheets, if they can write the respective TIFF
          Class X  files.   If your  application writes  all four  of these
          types, you  may wish to write it as _TIFF B,G,P,R._  Of course, a
          term like  _TIFF B,_  while fine  for  communicating  with  other
          vendors, will  not convey much information to a typical user.  In
          this case,  a  phrase  such  as  _Standard  TIFF  Black-and-White
          Scanned Images_ might be better.
          
          The same  terminology guidelines  apply to applications that read
          TIFF Class X files.
          
          If your  application reads more kinds of files than it writes, or
          vice versa,  it would  be a  good idea  to make that clear to the
          buyer.   For example, if your application reads TIFF B and TIFF G










          TIFF 5.0                                          page 57          TIFF 5.0                                          page 57


          files, but writes only TIFF G files, you should write it that way
          in the spec sheet.
          




























































          TIFF 5.0                                          page 58          TIFF 5.0                                          page 58


          Appendix H: Image Colorimetry Information
          
          Chris Sears
          210 Lake Street
          San Francisco, CA 94118
          
          June 4, 1988
          Revised August 8, 1988
          
          
          I. Introduction
          
          Our goal is to accurately reproduce a color image using different
          devices.   Accuracy requires  techniques  of  measurement  and  a
          standard  of   comparison.     Different  devices   imply  device
          independence.   Colorimetry provides the framework to solve these
          problems.  When an image has a complete colorimetric description,
          in principle  it  can  be  reproduced  identically  on  different
          monitors and using different media, such as offset lithography.
          
          The colorimetry  data is  specified when  the image is created or
          changed.   A scanned image has colorimetry data derived from  the
          filters and  light sources  of the  scanner and a synthetic image
          has colorimetry  data corresponding to the monitor used to create
          it or  the monitor model of the rendering environment.  This data
          is used  to map  an input  image to  the markings  or colors of a
          particular output device.
          
          Section II  describes various  standards organizations  and their
          work in color.
          Section III describes our motivation for seeking these tags.
          Section IV describes our goals of reproduction.
          Sections V, VI and VII introduce the colorimetry tags.
          Section VIII specifies the tags themselves.
          Section IX describes the defaults.
          Section X discusses the limitations and some of the other issues.
          Section XI provides a few references.
          
          
          II. Related Standards
          
          TIFF is  a general  standard for describing image data.  It would
          be foolish  for us  to change  TIFF in  a way  that did not match
          existing industry  and international  standards.   Therefore,  we
          have taken  pains to  note in the discussion below the efforts of
          various standards organizations and select defaults from the work
          of these organizations.
          
          CIE  (Commission Internationale de l’Eclairage)  The basis of the
          colorimetry information  is the  CIE 1931  Standard Observer [3].
          While other color models could be supported [1] [4], CIE 1931 XYZ
          is the  international standard  accepted  across  industries  for
          specifying  color   and  CIE  xyY  is  the  chromaticity  diagram
          associated with CIE 1931 XYZ tristimulus values.









          TIFF 5.0                                          page 59          TIFF 5.0                                          page 59


          
          NTSC (National Television  System Committee)  NTSC is of interest
          primarily  for   historical  reasons  and  its  use  in  encoding
          television data.   Manufacturing  standards for monitors have for
          some time  drifted significantly  from the  1953 NTSC colorimetry
          specification.
          
          SMPTE     (Society of  Motion Picture  and Television  Engineers)
          Most of  the work  by NTSC  has been  largely subsumed  by SMPTE.
          This organization  has a  set of  standards  called  "Recommended
          Practices" that  apply to  various technical  aspects of film and
          television production [5] [6].
          
          ISO  (International  Standards  Organization)    ISO  has  become
          involved in  color standards  through work on a color addendum to
          "Office Document Architecture (ODA) and Interchange Format" [7].
          
          ANSI (American  National   Standards  Institute)    ANSI  is  the
          American representative to ISO .
          
          
          III. Motivation
          
          Our motivation  for defining  these tags  stems from our research
          and  development  in  color  separation  technology.    With  the
          information described here and the RGB pixel data, we have all of
          the  information  necessary  for  generating  high-quality  color
          separations.  We could supply the colorimetry information outside
          of the  image  file.    But  since  TIFF  provides  a  convenient
          mechanism for  bundling all  of the  relevant  information  in  a
          single place,  tags are  defined to  describe this information in
          color TIFF files.
          
          A color  image rendered  with incorrect  colorimetry  information
          looks different  from the original.  One of our early test images
          has an artifact in it where the image was scanned with one set of
          primaries and  color ramps  were  overlaid  on  top  of  it  with
          different primaries.  The blue ramp looked purple when we printed
          it. Using incorrect gamma tables or white points can also lead to
          distorted images.  The best way to avoid these kinds of errors is
          to allow  the creator  of an  image  to  supply  the  colorimetry
          information along with the RGB values [1] [2].
          
          The purpose  of the  colorimetry data  is to  allow a  projective
          transformation from the primaries and white point of the image to
          the primaries  and white  point of  the rendering  media.   Gamma
          reflects the non-linear transfer gradient of real media.
          
          
          IV. Colorimetric Color Reproduction
          
          Earlier we  said that given the proper colorimetric data an image
          could be  rendered identically  using  two  different  calibrated
          devices.   By identical,  we mean  colorimetric reproduction [9].









          TIFF 5.0                                          page 60          TIFF 5.0                                          page 60


          Specifically, the  chromaticities  match  and  the  luminance  is
          scaled to correspond to the luminance range of the output device.
          Because of this, we only need the chromaticity coordinates of the
          white point  and primaries.   The absolute luminance is arbitrary
          and unnecessary.
          
          
          V. White Point
          
          In TIFF 4.0, the white point was specified as D65.  This appendix
          allocates a  separate tag  for describing the white point and D65
          is the logical default since it is the SMPTE standard [6].
          
          The white  point is  defined  colorimetrically  in  the  CIE  xyY
          chromaticity diagram.   While  it is  rare for monitors to differ
          from D65,  scanned images  often  have  different  white  points.
          Rendered images  can have  arbitrary white  points.   The graphic
          arts use D50 as the standard viewing light source [8].
          
          
          VI. Primary Chromaticities
          
          In TIFF  4.0, the  primary color  chromaticities matched the NTSC
          specification.  With the wide variety of color scanners, monitors
          and renderers,  TIFF needs  a mechanism for accurately describing
          the chromaticities  of the  primary colors.   We use SMPTE as the
          default chromaticity  since conventional  monitors are  closer to
          SMPTE and  some monitors  (Conrac 6545)  are manufactured  to the
          SMPTE specifications.   We  don’t use the NTSC chromaticities and
          white point  because present day monitors don’t use them and must
          be _matrixed_ to approximate them.
          
          As an  example, the primary color chromaticities used by the Sony
          Trinatron differ  from those  recommended by  SMPTE.  In general,
          since  real  monitors  vary  from  the  industry  standards,  the
          chromaticities of  primaries are described in the CIE xyY system.
          This  allows   a  reproduction   system  to  compensate  for  the
          differences.
          
          
          VII. Color Response Curves
          
          This tag  defines three  color response curves, one each for red,
          green, and blue color information.  The width of each entry is 16
          bits, as  implied by  the type  SHORT.   The minimum intensity is
          represented by 0 and the maximum by 65535.  For example, black is
          represented by  0,0,0 and  white by  65535, 65535,  65535.    The
          length of  each curve is 2**BitsPerSample.  A ColorResponseCurves
          field for RGB data where each of the samples is 8 bits deep would
          have 3*256  entries.   The 256  red  entries  would  come  first,
          followed by 256 green entries, followed by 256 blue entries.
          
          The purpose  of the  ColorResponseCurves field  is to  act  as  a
          lookup table  mapping sample values to specific intensity values,









          TIFF 5.0                                          page 61          TIFF 5.0                                          page 61


          so that  an image  created on  one system  can  be  displayed  on
          another   with   minimal   loss   of   color   fidelity.      The
          ColorResponseCurves field thus describes the _gamma_ of an image,
          so that  a TIFF  reader on another system can compensate for both
          the image gamma and the gamma of the reading system.
          
          Gamma is  a term that relates to the typically nonlinear response
          of most  display devices,  including monitors.   In  most display
          systems, the  voltage applied to the CRT is directly proportional
          to the  value of  the red,  green, or  blue sample.  However, the
          resulting luminance  emitted by  the  phosphor  is  not  directly
          proportional to  the voltage.   This relationship is approximated
          in most displays by
          
               luminance = voltage ** gamma
          
          The NTSC  standard gamma  of 2.2 adequately describes most common
          video systems.  The standard  gamma of  2.2 implies a dim viewing
          surround.   (We know of no SMPTE recommended practice for gamma.)
          The following example uses an 8 bit sample with value of 127.
          
               voltage = 127 / 255 = 0.4980
               luminance = 0.4980 ** 2.2 = 0.2157
          
          In the  examples below,  we only  consider a  single primary  and
          therefore only a single curve.  The same analysis applies to each
          of the  red, green,  and blue  primaries and  curves.   Also, and
          without loss  of generality,  we assume that there is no hardware
          color map, so that we must alter the pixel values themselves.  If
          there is  a color  map, the  manipulations can be done on the map
          instead of on the pixels.
          
          If no  ColorResponseCurves field  exists in  a color  image,  the
          reader should  assume a  gamma of  2.2 for each of the primaries.
          This default curve can be generated with the following C code:
          
               ValuesPerSample = 1 << BitsPerSample;
               for (curve[0] = 0, i = 1; i < ValuesPerSample; i++)
                    curve[i] =  floor (pow  (i /  (ValuesPerSample -  1.0),
          2.2) * 65535.0 + .5);
          
          The displaying  or rendering  application can know its own gamma,
          which we  will call  the _destination  gamma._   (An uncalibrated
          system can usually assume that its gamma is 2.2 without going too
          far  wrong.)     Using   this  information  the  application  can
          compensate for the gamma of the image, as we shall see below.
          
          If  the  source  and  destination  systems  are  both  adequately
          described  by   a  gamma  of  2.2,  the  writer  would  omit  the
          ColorResponseCurves field,  and the  reader can  simply read  the
          image directly into the frame buffer.  If a writer writes out the
          ColorResponseCurves field,  then a  reader must  assume that  the
          gammas  differ.    A  reader  must  then  perform  the  following
          computation on each sample in the image:









          TIFF 5.0                                          page 62          TIFF 5.0                                          page 62


          
               NewSampleValue  =   floor  (pow   (curve[OldSampleValue]   /
          65535.0, 1.0 / DestinationGamma) *
                 (ValuesPerSample - 1.0) + .5);
          
          Of course,  if the _gamma_ of the destination system is not well-
          approximated with  an exponential  function, an  arbitrary  table
          lookup may  be used  in place  of raising  the  value  to  1.0  /
          DestinationGamma.
          
          Leave out  ColorResponseCurves if  using the default gamma.  This
          saves about  1.5K in  the  most  common  case,  and,  after  all,
          omission is the better part of compression.
          
          Do not  use this  field to  store frame  buffer color  maps.  Use
          instead   the    ColorMap   field.       Note,    however,   that
          ColorResponseCurves may  be used  to refine  the information in a
          ColorMap if desired.
          
          The above  examples assume  that a  single parameter gamma system
          adequately approximates the response characteristics of the image
          source and  destination systems.   This will usually be true, but
          our use  of a table instead of a single gamma parameter gives the
          flexibility  to  describe  more  complex  relationships,  without
          requiring additional computation or complexity.
          
          
          VIII. New Tags and Changes
          The following tags should be placed in the "Basic Fields" section
          of
          the TIFF specification:
          
          White Point
          Tag  = 318 (13E)
          Type = RATIONAL
          N    = 2
          
          The white  point of the image.  Note that this value is described
          using  the  1931  CIE  xyY  chromaticity  diagram  and  only  the
          chromaticity is  specified.  The luminance component is arbitrary
          and not  specified.   This can correspond to the white point of a
          monitor that  the image  was painted  on,  the  filter  set/light
          source combination  of a  scanner, or  to the  white point of the
          illumination model of a rendering package.
          
          Default is the SMPTE white point, D65:  x = 0.313, y = 0.329.
          
          The ordering is x, y.
          
          
          PrimaryChromaticities
          Tag  = 319 (13F)
          Type = RATIONAL
          N    = 6









          TIFF 5.0                                          page 63          TIFF 5.0                                          page 63


          
          The primary  color chromaticities.   Note  that these  values are
          described using  the 1931  CIE xyY  chromaticity diagram and only
          the chromaticities  are  specified.    For  paint  images,  these
          represent the  chromaticities of  the  monitor  and  for  scanned
          images  they   are  derived  from  the  filter  set/light  source
          combination of a scanner.
          
          Default is the SMPTE primary color chromaticities:
          
               Red: x = 0.635 y = 0.340
               Green:    x = 0.305 y = 0.595
               Blue:     x = 0.155 y = 0.070
          
          The ordering is red x, red y, green x, green y, blue x, blue y.
          
          Color Response Curves
          
          Default for  ColorResponseCurves represents  curves corresponding
          to the NTSC standard gamma of 2.2.
          
          
          IX. Defaults
          
          The defaults  used by  TIFF reflect industry standards.  Both the
          WhitePoint and  PrimaryChromaticities tags have defaults that are
          promoted  by   SMPTE  .     In  addition,  the  default  for  the
          ColorResponseCurves tag matches the NTSC specification of a gamma
          of 2.2.
          
          The purpose  of these  defaults is to allow reasonable results in
          the absence  of  accurate  colorimetry  data.    An  uncalibrated
          scanner or  paint system  produces an  image  that  be  displayed
          identically, though  probably incorrectly  on two  different  but
          calibrated systems.   This is better then the uncertain situation
          where the  image might  be rendered  differently on two different
          but calibrated systems.
          
          
          X. Limitations and Issues
          
          This section  discusses several  of the  limitations  and  issues
          involved in colorimetric reproduction.
          
          Scope of Usefulness
          
          For many  purposes the  data recommended  here is unnecessary and
          can be omitted.  For presentation graphics where there are only a
          few colors,  being able  to tell  red from green is probably good
          enough.   In this  case the  tags can  be ignored and there is no
          overhead.   In more  demanding color  reproduction  environments,
          this data  allows images to be described device independently and
          at small cost.
          









          TIFF 5.0                                          page 64          TIFF 5.0                                          page 64


          User Burdens
          
          The data we recommend isn’t a user burden; it is really a systems
          issue.   It allows  a systems  solution but  doesn’t require user
          intercession.   Calibration however  is a  separate issue.  It is
          likely to involve the user.
          
          Resolution Versus Fidelity
          
          Some manufacturers  supply greater than 24 bits of resolution for
          color specification.   The  purpose of  this is  either to  avoid
          artifacts such  as contouring  in the shadows or in some cases to
          be more  specific or  device independent  about the  color.  Both
          reasons can  be misguided.   Other, less expensive techniques can
          be used  to prevent artifacts, such as deeper color maps.  As for
          accuracy, fidelity is more important than precision.
          
          Colorimetric Color Reproduction
          
          There are other choices for objectives of color reproduction [9].
          Spectral color  reproduction is a stronger condition and most are
          weaker, such  as preferred  color  reproduction.    While  device
          independent spectral  color reproduction  is  impossible,  device
          independent  colorimetric  reproduction  is  possible,  within  a
          tolerance and within the limits of the gamuts of the devices.  By
          choosing a  strong criteria  we allow the important objectives of
          weaker criteria, such as preferred color reproduction, to be part
          of design packages.
          
          Metamerism
          
          If two  patches of  color  are  identical  under  one  light  and
          different under  another, they  are said  to be  metameric pairs.
          Colorimetric  color  reproduction  is  a  weaker  condition  than
          spectral color reproduction and hence allows metamerism problems.
          By standardizing  the viewing  conditions we  can largely finesse
          the metamerism  problem for  print.   Because television is self-
          luminous and doesn’t use spectral absorption, metamerism isn’t so
          much a problem.
          
          Color Models - xyY Versus Luv, etc.
          
          We choose  xyY over  Luv [1]  because XYZ  is  the  international
          standard for  color specification  and xyY  is  the  chromaticity
          diagram associated  with XYZ.   Luv is meant for color difference
          measurement.
          
          Ambient Environment And Viewing Surrounds
          
          The viewing environment affects how the eye perceives color.  The
          eye adapts  to a  dark room  and it adapts to a colored surround.
          While  these   problems  can   be  compensated   for  within  the
          colorimetric framework  [4], it is much better to finesse them by
          standardizing.   The design environment should match the intended









          TIFF 5.0                                          page 65          TIFF 5.0                                          page 65


          viewing environment.   Specifically it should not be a pitch dark
          room and,  on average,  it should  be of  a neutral  color.   For
          print, ANSI recommends a Munsell N-8 surface [8].
          
          
          XI. References
          
          In particular,  we would  like to mention the work of Stuart Ring
          of the  Copy Products  Division of the Eastman Kodak Company.  He
          and  his  colleagues  are  promoting  a  color  data  interchange
          paradigm.   They are  working closely  with the  ISO 8613 Working
          Group [7].
          
          [1]  Color Data  Interchange Paradigm,  Eastman Kodak, Rochester,
          New York, 7 December 1987.
          
          [2]  Color  Reproduction   and  Illumination  Models,  Roy  Hall,
          International Summer  Institute:   State of  the Art  in Computer
          Graphics, 1986.
          
          [3]  CIE   Colorimetry:    Official   Recommendations    of   the
          International Commission on Illumination, Publication 15-2, 1986.
          
          [4]  Color Science:  Concepts and  Methods, Quantitative Data and
          Formulae, Gunter  Wyszecki, W.S.  Stiles, John  Wiley  and  Sons,
          Inc., New York, New York, 1982.
          
          [5]  Color Monitor  Colorimetry, SMPTE  Recommended  Practice  RP
          145-1987.
          
          [6]  Color Temperature  for  Color  Television  Studio  Monitors,
          SMPTE Recommended Practice RP 37.
          
          [7]  Office   Document   Architecture   (ODA)   and   Interchange
          Format_Addendum on Colour, ISO 8613 Working Draft.
          
          [8]  ANSI Standard PH 2.30-1985.
          
          [9]  The Reproduction  of Colour  in  Photography,  Printing  and
          Television, R.  W. G.  Hunt, Fountain  Press, Tolworth,  England,
          1987.
          
          [10] Raster  Graphics   Handbook,  The  Conrac  Corporation,  Van
          Nostrand Reinhold  Company, New  York,  New  York,  1985.    Good
          description of gamma.
          
          
          















          TIFF 5.0                                          page 66          TIFF 5.0                                          page 66


          Appendix I:  Horizontal Differencing Predictor
          
          
          This appendix,  written after  the release of Revision 5.0 of the
          TIFF specification,  is still  in draft  form.   Please send  any
          comments to the Aldus Developers Desk.
          
          
          Revision 5.0  of the  TIFF specification defined a new tag called
          _Predictor_  that  describes  techniques  that  may  be  used  in
          conjuction with  TIFF compression  schemes.    We  now  define  a
          Predictor that  greatly  improves  compression  ratios  for  some
          images.
          
          The horizontal  differencing predictor  is assigned the tag value
          Predictor = 2:
          
          Predictor
          Tag  = 317 (13D)
          Type = SHORT
          N    = 1
          
          A predictor  a mathematical operator that is applied to the image
          data before  the encoding  scheme is  applied.   Currently (as of
          revision 5.0)  this tag  is used  only with  LZW  (Compression=5)
          encoding, since  LZW is  probably the  only TIFF  encoding scheme
          that benefits  significantly from a predictor step.  See Appendix
          F.
          
          1 = No prediction scheme used before coding.
          2 = Horizontal differencing. See Appendix I.
          
          Default is 1.
          
          
          The algorithm
          
          The idea  is to  make use  of the  fact that many continuous tone
          images rarely  vary much  in pixel  value from  one pixel  to the
          next.   In such  images,  if  we  replace  the  pixel  values  by
          differences between  consecutive pixels,  many of the differences
          should be  0, plus  or minus  1, and  so on.   This  reduces  the
          apparent information  content, and  thus allows LZW to encode the
          data more compactly.
          
          Assuming 8-bit  grayscale  pixels  for  the  moment,  a  basic  C
          implementation might look something like this:
          
               char image[ ][ ];
               int  row, col;
          
               /* take horizontal differences:
                */
               for (row = 0; row < nrows; row++)









          TIFF 5.0                                          page 67          TIFF 5.0                                          page 67


                    for (col = ncols - 1; col >= 1; col--)
                         image[row][col] -= image[row][col-1];
          
          If we  don_t have 8-bit samples, we need to work a little harder,
          so that  we can make better use of the architecture of most CPUs.
          Suppose we  have 4-bit  samples, packed  two to a byte, in normal
          TIFF uncompressed  (i.e., Compression=1)  fashion.   In order  to
          find differences,  we want to first expand each 4-bit sample into
          an 8-bit  byte, so  that we  have one  sample per byte, low-order
          justified.   We then  perform the  above horizontal differencing.
          Once the  differencing has  been completed, we then repack the 4-
          bit differences  two to  a  byte,  in  normal  TIFF  uncompressed
          fashion.
          
          If the  samples are  greater than  8  bits  deep,  expanding  the
          samples into  16-bit words  instead of 8-bit bytes seems like the
          best way to perform the subtraction on most computers.
          
          Note that we have not lost any data up to this point, nor will we
          lose any  data later  on.   It  might  at  first  seem  that  our
          differencing might  turn 8-bit samples into 9-bit differences, 4-
          bit samples  into 5-bit differences, and so on.  But it turns out
          that we  can completely  ignore the  _overflow_  bits  caused  by
          subtracting a  larger number  from a  smaller  number  and  still
          reverse the  process  without  error.    Normal  twos  complement
          arithmetic does just what we want.  Try an example by hand if you
          need more convincing.
          
          Up  to  this  point  we  have  implicitly  assumed  that  we  are
          compressing  bilevel   or  grayscale   images.     An  additional
          consideration arises in the case of color images.
          
          If PlanarConfiguration  is 2,  there is no problem.  Differencing
          proceeds the same way as it would for grayscale data.
          
          If  PlanarConfiguration  is  1,  however,  things  get  a  little
          trickier.   If  we  didn’t  do  anything  special,  we  would  be
          subtracting red  sample values  from green  sample values,  green
          sample values  from blue  sample values,  and blue  sample values
          from red sample values, which would not give the LZW coding stage
          much redundancy  to work  with.   So we  will do  our  horizontal
          differences with  an offset  of SamplesPerPixel  (3, in  the  RGB
          case).  In other words, we will subtract red from red, green from
          green, and  blue from blue.  The LZW coding stage is identical to
          the SamplesPerPixel=1 case.  We require that BitsPerSample be the
          same for all 3 samples.
          
          
          Results and guidelines
          
          LZW without  differencing works  well  for  1-bit  images,  4-bit
          grayscale images, and synthetic color images.  But natural 24-bit
          color images  and some 8-bit grayscale images do much better with
          differencing.  For example, our 24-bit natural test images hardly









          TIFF 5.0                                          page 68          TIFF 5.0                                          page 68


          compressed at  all using  _plain_ LZW:  the  average  compression
          ratio was  1.04  to  1.    The  average  compression  ratio  with
          horizontal differencing  was 1.40  to 1.  (A compression ratio of
          1.40 to 1 means that if the uncompressed image is 1.40MB in size,
          the compressed version is 1MB in size.)
          
          Although  the   combination  of   LZW  coding   with   horizontal
          differencing does  not result  in any  loss of  data, it  may  be
          worthwhile in  some situations  to give  up some  information  by
          removing as  much noise  as possible  from the  image data before
          doing the  differencing, especially  with  8-bit  samples.    The
          simplest way  to get  rid of noise is to mask off one or two low-
          order bits  of each 8-bit sample.  On our 24-bit test images, LZW
          with horizontal differencing yielded an average compression ratio
          of 1.4 to 1.  When the low-order bit was masked from each sample,
          the compression  ratio climbed to 1.8 to 1; the compression ratio
          was 2.4  to 1  when masking  two bits,  and 3.4 to 1 when masking
          three bits.   Of  course, the  more you  mask, the  more you risk
          losing useful information along with the noise.  We encourage you
          to experiment  to find  the best compromise for your device.  For
          some applications it may be useful to let the user make the final
          decision.
          
          Interestingly, most  of our RGB images compressed slightly better
          using PlanarConfiguration=1.   One  might think  that compressing
          the  red,   green,  and   blue   difference   planes   separately
          (PlanarConfiguration=2) might  give  better  compression  results
          than  mixing   the  differences   together   before   compressing
          (PlanarConfiguration=1), but this does not appear to be the case.
          
          Incidentally,  we  tried  taking  both  horizontal  and  vertical
          differences,  but   the  extra   complexity  of   two-dimensional
          differencing did  not appear  to pay  off for  most of  our  test
          images.  About one third of the images compressed slightly better
          with two-dimensional  differencing, about  one  third  compressed
          slightly worse, and the rest were about the same.
          
          
          
          
          






















          TIFF 5.0                                          page 69          TIFF 5.0                                          page 69


          Appendix J:  Palette Color
          
          
          This appendix,  written after  the release of Revision 5.0 of the
          TIFF specification,  is still  in draft  form.   Please send  any
          comments to the Aldus Developers Desk.
          
          
          Revision  5.0   of  the   TIFF  specification   defined   a   new
          PhotometricInterpretation value  called _palette color._  We have
          been wondering  lately if this additional complexity is worth the
          implementation expense.   If  not, let_s  drop it before too many
          people start creating palette color images.
          
          
          The Proposal
          
          Instead of a separate palette color image type, there seems to be
          no compelling reason why palette (mapped) color images should not
          be stored as _full color_ (usually 24-bit) RGB images.
          
          
          Objections
          
          The most  obvious objection is the amount of space required.  But
          if you  care about how much space the image takes up on disk, you
          should use  LZW compression,  which is  ideally  suited  to  most
          palette color  images.   (LZW compresses  most paint-type palette
          color images  5:1 or  more.)   And if you use LZW compression, it
          turns out  that palette  color images stored as full color images
          compress to  almost exactly the same size as palette color images
          stored as  palette color  images.  That is, with LZW compression,
          there is  no penalty  for storing  palette color  images as  full
          color RGB  images.   The resulting  file may  be  a  few  percent
          larger, but  it will not be three times as large.  See Appendix F
          for more information on how LZW works.
          
          Another objection  might be  that an  application might  want  to
          process the  image differently  if it is _really_ a palette color
          image. But  we can easily add auxiliary information that can help
          a TIFF  reader to quickly categorize color images if it wants to.
          See the _New tags_ section below.
          
          
          Benefits
          
          It may  be obvious,  but it  is probably  worth discussing why we
          want  to   abolish   palette   color   images   as   a   distinct
          classification.
          
          The main  problem is  that palette color as a separate type makes
          life more  hazardous and  confusing for  users.    The  confusion
          factor is  aggravated because  users already  have to be somewhat
          aware of  distinctions  between  bilevel,  grayscale,  and  color









          TIFF 5.0                                          page 70          TIFF 5.0                                          page 70


          images.   Having two  main types of color images is hard for many
          users to  grasp, and  it is probably not possible to totally hide
          this complexity  from the user in certain situations.  The hazard
          level goes  up because some applications may accept palette color
          but not  full color  images, or  full color but not palette color
          images, or may accept 8-bit palette color images but not 4-bit or
          3-bit palette color images.
          
          The second  problem is  that writing and maintaining code to deal
          with an  additional image  type is  somewhat expensive  for  TIFF
          readers.  The cost of supporting palette color images will depend
          on the  application, but  we believe  that, in  general, the cost
          will be  substantial.   It seems  to make  more sense  to put the
          burden on  TIFF writers to convert palette color images into full
          color image  form than  to make TIFF readers handle an additional
          color image  type, since there are more TIFF readers than writers
          at this point.
          
          
          New tags
          
          Here are  some proposed  new tags that can help to classify color
          images, and  make up  for not  having a  separate  palette  color
          class.  They are not required for TIFF Class R , but are strongly
          recommended for  color TIFF  images created by palette-type color
          paint programs.
          
          ColorImageType
          Tag  = 318 (13E)
          Type = SHORT
          N    = 1
          
          Gives TIFF  color image  readers a  better idea  of what  kind of
          color image it is.  There will be borderline cases.
          
          1 = Continuous tone, natural image.
          2 =  Synthetic image, using a greatly restricted range of colors.
          Such images  are produced  by most  color paint  programs.    See
          ColorList for a list of colors used in this image.
          
          Default is 1.
          
          ColorList
          Tag  = 319 (13F)
          Type = BYTE or SHORT
          N    = the  number of  colors that  are used in this image, times
          SamplesPerPixel
          
          A list  of colors that are used in this image.  Use of this field
          is only  practical for  images containing  a  greatly  restricted
          (usually  less   than  or   equal  to   256)  range   of  colors.
          ColorImageType should be 2.  See ColorImageType.
          










          TIFF 5.0                                          page 71          TIFF 5.0                                          page 71


          The list  is organized  as an array of RGB triplets, with no pad.
          The RGB  triplets are  not guaranteed  to be  in  any  particular
          order.   Note that the red, green, and blue components can either
          be a  BYTE or  a SHORT  in length.  BYTE should be sufficient for
          most applications.
          
          No default.